## Slide 1: OPC
Ramoncito

## Slide 2: OPC - Early computers
PROGRAM-CONTROLLED COMPUTERS – These computers (1938-1949) were programmed by setting switches and inserting patch cables.
Primitive architecture –CPU, ALU, registers, I/O devices, storage units?, etc.,….
  Every configuration of switches and patch cables conformed an instruction. Each instruction was wired, then the program.
  The electric storage units and I/O devices ranged from very primitive to something better, for a short time.
  No OS.

## Slide 3: PROGRAM-CONTROLLED COMPUTERS
Sin SO

## Slide 4: Context of a current Computer
Current architecture –CPU (control unit), ALU, registers, storage unit, I/O devices, etc.,….
VON NEUMANN’S –
  The addition of a stored-program in a single separate memory structure that keeps both instructions and data.
  The computers that follow the "von Neumann architecture" are also known as the "stored-program computer“.
Registers

## Slide 5: Hardware moderno con Bus
Componentes de una computadora básica
  Exceptuando el CPU, cada uno de los componentes tiene un controlador
  Cada controlador posee: registros y un buffer, para realizar las entradas y / o las salidas.
  El bus tiene tres canales: datos, direcciones de memoria y señales de control.
BUS
Monitor
controller

## Slide 6: A Desktop Computer with USB
BUS
controller
Controlador
  Permite hacer intercambio de información entre los distintos dispositivos.
  El CPU se comunica con los controladores.
  Driver: subrutina (software) del Kernel que maneja al controlador de un dispositivo.

## Slide 7: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip

## Slide 8: Computer System Components (layers)
Command Interpreter?
Kernel
Instructions?
Software
O.S.
Basic Routines

## Slide 9: Computer System Components
Users (people, machines, other computers) captcha: distinguishes human from machine input
System and Applications programs : System programs – help the users to develop applications (compilers, assemblers, database systems, line text editors, etc.), Command Interpreter. Applications programs – help the users to solve their computing problems (spreadsheets, web explorers, video games, business programs, word processors, function libraries). -Software-.
Basic Routines – controls and coordinates the use of the hardware among the various application programs for the various users. For these tasks contains programs and subprograms (kernel) -Software-.
Hardware – provides basic computing resources (CPU, memory, I/O devices)

## Slide 10: Computer Hardware
Which ones are the main functions / services of the Computer Hardware?
  __________________
  __________________
  __________________

## Slide 11: Referencias
Chapters: Tanenbaum, Operating Systems.
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Ago-Dic 2022

## Slide 12: OPC - Basic Concepts: Overview
Computer Structure - hardware
Assembly Language
Data Representation

## Slide 13: General Computer Structure
*PC
CPU
Buffers
I/O Module Controllers
Central
Memory
Instruction
Instruction
Instruction
Data
Data
Data
Data
.
.
.
.
.
IR
MAR
MBR
I/O AR
I/O BR
execution
unit
.
.
.
.
.
.
MAR - Memory Address Register
MBR - Memory Buffer Register
I/O AR - I/O Address Register
I/O BE - I/O Buffer Register
PC - Program Counter
IR - Instruction Register
SP – Stack Pointer
PSW – Process Status Word
*Must be saved and restored
0
N
1
*SP
*PSW
BUS
Stored-program

## Slide 14: Central Memory
Conformed by RAM
Ordered collection of bytes (like a vector)
Memory address as index of a byte
Each byte of the memory has a memory address for access

## Slide 15: Ejecución de Programas en Leng. Alto Nivel
Flujo para ejecutar programas en C / C++:
  Compilar con el Compilador, prog.cc a prog.obj
  Ligado o vinculado (linking) con el Linker, prog.obj a prog.exe
  Ejecución de programa prog.exe
prog.cc
Compilador
prog.obj
prog.exe
Linker
Programa fuente
Programa objeto
Programa ejecutable

## Slide 16: Translating Languages
English: Display the sum of A times B plus C.
C++: F = A * B + C;
cout << (F);
Assembly Language:
mov EAX, A
mul B
add EAX, C
mov F, EAX
call WriteInt
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
- - - -
E8 00500000

## Slide 17: Compilación de Alto Nivel a Ensamblador
Flujo para producir programas Ensamblador desde C / C++:
  Compilar con el Compilador, con opción ensamblador,
  de prog.cc a prog.asm
prog.cc
Compilador
prog.asm
Programa fuente
Programa ensamblador

## Slide 18: Ejecución de Programas en Leng. Ensamblador
Flujo para ejecutar programas en Ensamblador:
  Ensamble con el Ensamblador, prog.asm a prog.obj
  Ligado o vinculado (linking) con el Linker, prog.obj a prog.exe
  Ejecución de programa prog.exe
prog.asm
Ensamblador
prog.obj
prog.exe
Linker
Programa fuente
Programa objeto
Programa ejecutable

## Slide 19: Assembly Language (AL)
What is an Assembler (Ensamblador)?
What background should I have?
How does Assembly Language (AL) relate to machine language?
How do C++ and Java relate to AL?
Is AL portable?

## Slide 20: Assembly Data Representation
Binary Numbers
Binary Addition
Integers
Storage Sizes
Unsigned Integers
Hexadecimal Integers

## Slide 21: Binary Numbers
Binary Digits are 1 and 0
  1 = true
  0 = false
MSB – most significant bit
LSB – least significant bit
Bit numbering:

## Slide 22: Unsigned Binary Numbers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:
Every binary number is a sum of powers of 2

## Slide 23: Translating Binary to Decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
dec = (Bn-1  2n-1) + (Bn-2  2n-2) + ... + (B1  21) + (B0  20)
B = binary digit
binary 00001001 = decimal ??:
(02  27) + (02  26) + (02  25) + (02  24) +
(12  23) + (02  22) + (02  21) + (12  20) = 910

## Slide 24: Translating Unsigned Decimal to Binary
37 = 100101
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:
3710 = 1001012
B0
B1
B2
B3
B4
B5

## Slide 25: Binary Addition
Starting with the LSB, add each pair of digits, include the carry if present.

## Slide 26: Integers and Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 27: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 28: Translating Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer
  0001 0110 1010 0111 1001 01002 to hexadecimal:

## Slide 29: Powers of 16
Used when calculating hexadecimal values up to n digits long:

## Slide 30: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16:
  dec = (H3  163) + (H2  162) + (H1  161) + (H0  160)
Hex 123416 equals (1  163) + (2  162) + (3  161) + (4  160), or decimal 4,66010.
Hex 3BA416 equals (3  163) + (11 * 162) + (10  161) + (4  160), or decimal 15,26810.

## Slide 31: Converting Decimal to Hexadecimal
decimal 42210 = 1A616 hexadecimal
H0
H1
H2

## Slide 32: Hexadecimal Addition
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.
36 28 28 6A
42 45 58 4B
78 6D 80 B5
1
1
21 / 16 = 1, rem 5
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.

## Slide 33: Binary Subtraction
Subtract A – B
0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1
Practice: Subtract 0101 from 1001.

## Slide 34: Hexadecimal Subtraction
When a borrow is required from the digit to the left, add 16 (decimal) to the current digit's value:
C6 75
A2 47
24 ??
-1
16 + 5 = 21
Practice: The address of var1 is 00400020. The address of the next variable after var1 is 0040006A. How many bytes are used by var1?

## Slide 35: Referencias
Chapters: Tanenbaum, A. S.; Operating Systems.
Chapters: Irvine, Kip R.; Assembly Language for x86 Processors.
Notas: Ramón Ríos.
Agosto – diciembre 2022

## Slide 36: Ranges of Unsigned Integers
Standard sizes:

## Slide 37: Signed Integers
The highest bit (MSB) indicates the sign. 1 = negative, 0 = positive
If the highest digit of a hexadecimal integer is > 7, the value is negative. Examples: F5, 8A, C5, A2, 9D

## Slide 38: Ranges of Signed Integers
The highest bit is reserved for the sign. This limits the range:
Practice: What is the largest positive value that may be stored in 20 bits?

## Slide 39: Forming the Two's Complement
Negative numbers are stored in Two’s Complement notation
    1st : do One’s Complement with the number
    2nd: add 1 to the One’s Complemented number
Represents the additive Inverse
Note that 0000 0001 + 1111 1111 = 0000 0000

## Slide 40: Binary Subtraction
When subtracting A – B, convert B to its Two’s Complement.
Add A to (–B)
0 0 0 0 1 1 0 0 0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1 + 1 1 1 1 1 1 0 1
0 0 0 0 1 0 0 1

## Slide 41: Learn How To Do the Following:
Converting UNSIGNED and SIGNED Integers
Form the two's complement of a hexadecimal integer
Convert signed binary to decimal
Convert signed decimal to binary
Convert signed decimal to hexadecimal
Convert signed hexadecimal to decimal

## Slide 42: Hex One’s Complement
Hex |  | Bin |  | Bin C1s |  | Hex C1s
0 | > | 0000 | C1s | 1111 | > | F
1 | > | 0001 | C1s | 1110 | > | E
2 | > | 0010 | C1s | 1101 | > | D
3 | > | 0011 | C1s | 1100 | > | C
4 | > | 0100 | C1s | 1011 | > | B
5 | > | 0101 | C1s | 1010 | > | A
6 | > | 0110 | C1s | 1001 | > | 9
7 | > | 0111 | C1s | 1000 | > | 8
8 | > | 1000 | C1s | 0111 | > | 7
9 | > | 1001 | C1s | 0110 | > | 6
A | > | 1010 | C1s | 0101 | > | 5
B | > | 1011 | C1s | 0100 | > | 4
C | > | 1100 | C1s | 0011 | > | 3
D | > | 1101 | C1s | 0010 | > | 2
E | > | 1110 | C1s | 0001 | > | 1
F | > | 1111 | C1s | 0000 | > | 0

## Slide 43: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Agosto – diciembre 2022

## Slide 44: Arithmetic Operator Precedence
HLL operator precedence in evaluation of Arithmetic Expressions
1- ( )
2- - unary
3- *, /
4- +, -
Examples:
  X = 6 - Y * 5 + 2;
  R = -8 - T * (7 + M);

## Slide 45: Character Interpretation & Storage
Character sets
  Standard ASCII (0 – 127), 8 bits
    ‘u’, ‘U’, ‘A’, ‘8’, ‘2’
  Extended ASCII (0 – 255), 8 bits
  ANSI (0 – 255), 8 bits
  Unicode (0 – 65,535), 16 bits in Java

## Slide 46: Characters application
To type down a text command in a computer
To write down a computer program in a text file
To send messages
To send e-mails
. . .

## Slide 47: ASCII Code (7-bit) American Standard Code for Information Interchange

## Slide 48: Extended ASCII Code (8-bit)

## Slide 49: Characters use
Typing down “Hello”.
Hello
Chars stream
4816
6516
6C16
6C16
6F16

## Slide 50: HLL Strings in central memory
Two components
String
  Array of consecutive characters
  “Laura”
Null-terminated String
  A null (zero) character ending String
Interpretation and Storage
  Central memory ????

## Slide 51: Numeric Data Representation
pure binary
  can be calculated directly
ASCII char binary
  string of digits: "01010101"
ASCII char decimal
  string of digits: "65"
ASCII char hexadecimal
  string of digits: "9C"

## Slide 52: Boolean Operations
Easy to operate for ALU
Bit-to-bit
True:1, False:0
NOT
AND
OR
Operator Precedence
Truth Tables

## Slide 53: NOT
Inverts (reverses) a boolean value
One operand
If operator is T, then F; if F, then T
Truth table for Boolean NOT operator:
Digital gate diagram for NOT:

## Slide 54: AND
Two operands
Both must be T for T; otherwise F
Truth table for Boolean AND operator:
Digital gate diagram for AND:

## Slide 55: OR
Two operands
Both must be F for F; otherwise T
Truth table for Boolean OR operator:
Digital gate diagram for OR:

## Slide 56: Boolean Operator Precedence
56
The HLL order of evaluation is:
1.
Parentheses ( )
2.
NOT
3.
AND
4.
OR v
Example 1: F = A ^ (B v C) ^ (C v D)
Example 2: F = A ^ B v C ^ C v D

## Slide 57: NAND
Two operands
Both T, then F; otherwise T
Truth table for Boolean NAND operator:
Digital gate diagram for NAND:
X
Y
X NAND Y
F
F
T
T
F
T
F
T
T
T
T
F
NAND

## Slide 58: NOR
Two operands
Any T, then F; otherwise T
Truth table for Boolean NOR operator:
Digital gate diagram for NAND:
X
Y
X NOR Y
F
F
T
T
F
T
F
T
T
F
F
F
NOR

## Slide 59: Truth Tables
A Boolean function has one or more Boolean inputs, returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: X  Y

## Slide 60: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Agosto – diciembre 2022

## Slide 61: General Concepts
The Microprocessor
Cache Memory
Instruction execution cycle
Reading from Memory

## Slide 62: The Microprocessor - 1
Also called Central Processor Unit (CPU), the controlling element in a computer system
Control unit (CU) coordinates sequence of execution steps
  Controls memory and I/O through connections called buses
Arithmetic and Logic Unit (ALU) performs arithmetic and bitwise processing
Clock synchronizes CPU operations (oscillator)
Block diagram of a microcomputer
channel
channel
channel
controller
controller
controller

## Slide 63: The Microprocessor - 2
CU performs:
  data transfer between itself and the memory or I/O systems
  program flow via simple decisions, PC
ALU does:
  simple arithmetic and logic operations
  The resulting states of the ALU operations are placed in FLAGS (psw)

## Slide 64: Registers inside the CPU
Registers are hard-wired inside the CPU.
They can storage, 8-bit, 16-bit, 32-bit, 64-bit, or 128-bit long information (data or address).
Their speed access is very fast, and is the fastest in the computer hardware.

## Slide 65: Memory Storage Unit
Called Central or Main Memory
Mostly, made out of RAM chips
Storage, Addresses, Instructions and / or Data
Stored programs make the microprocessor and computer system very powerful devices
Conventional memory is outside the CPU, and it responds more slowly to access requests than registers

## Slide 66: Bus
A common group of wires that interconnect CPU, memory and I/O devices
Transfer control information, addresses, and data between components
Bus, containing three channels or sub-buses
  Control channel: determines where data comes from and goes, and ALU activities
  Address channel: selects where data comes from or goes to
  Data channel: moves data between memory bytes, I/O and CPU registers
channel
channel
channel
controller
controller
controller

## Slide 67: Clock (Oscillator)
Synchronizes all CPU and BUS operations
A tick every cycle
Machine (clock) cycle measures time of a single operation / instruction
Clock is used to trigger events

## Slide 68: Computer BUS
BUS has became a content element between all the components attached up
CPU has to compete, against other devices, to seize the memory unit (main, central, or RAM memory)
CPU needs to access the main memory to fetch next instruction and execute it up

## Slide 69: Cache Memory
Closer to the CPU
Access time: faster than Main Memory (RAM)
Storage size: smaller than Main Memory
Time to time: a block of Main Memory locations is copied, by CPU, to Cache Memory

## Slide 70: Main Memory <> Cache Memory
Sistemas Operativos
70
Memory
Address
1
3
0
2
2n - 1
Block
Block
(k words)
Word Length
Slot
Number
Tag
Block
0
2
1
C - 1
Block Length
(k words)
(a) Main Memory
(b) Cache Memory

## Slide 71: Issue
What issue arises from having a Main Memory and a Cache Memory? _____

## Slide 72: Storage Hierarchy
Storage systems organized, in hierarchy, by
  Access Speed ____
  Cost per bit ____
  Storage Size _____

## Slide 73: Instruction Execution Cycle
Loop
Instruc Fetch
Decode
Fetch operands
Execute
Store output
Repeat Loop until
HALT

## Slide 74: Reading from Memory
Multiple machine cycles are required when reading from memory, because it responds much more slowly than the CPU. The steps are:
  Execution step
  Cycle 1: address placed on address bus
  Cycle 2: Read Line (RD) set low (0), changing the value of processor’s RD
  Cycle 3: CPU waits one cycle for memory chips to respond
  Cycle 4: Read Line (RD) goes to 1, indicating that the data is on the data bus and can be copied
Memory Read Cycle

## Slide 75: Referencias
Chapters: Irvine, Kip R., Assembly Language for x86 Processors.
Chapters: Brey, Barry B., The Intel Microprocessors
Notas de Ramón Ríos.
Agosto – diciembre 2022

## Slide 76: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 77: Main, or Central, Memory
Main Memory structure
  A Linear Vector of Memory Bytes (content), with the indexes being the memory addresses to Access the content of the Memory Bytes
Hardware components
  EEPROMs
  xRAMs (e.g. DRAM)
  Device Controllers: each one with Control Registers and a Data Buffer

## Slide 78: Memory Layout for Multiprogrammed System

## Slide 79: Numerical Values: meanings
Data content: unsigned and signed values
  Registers
  Memory Byte locations
Memory Addresses
  To Access Memory Byte locations
  Represented as numerical unsigned values

## Slide 80: Multiple Memory Byte Values
Byte Values used as Data
One-byte content
Two-byte content
Four-byte content
Eight-byte content
Always Powers of 2, content

## Slide 81: Main Memory Addressing

## Slide 82: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Agosto – diciembre 2022

## Slide 83: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 84: Intel Microprocessor Evolution
Intel 8080, 8088
Intel 8086
Intel 80286
IA-32 processor family
Data and Addresses in BUS´s channels
Microprocessors / Computer Systems

## Slide 85: Early Intel Microprocessors
Intel 8080
  8-bit registers, 32-bit integers
  64KB addressable RAM (____-bit addressing)
  S-100 BUS architecture, 8-bit data bus
  MS-DOS Operating System
  8-inch floppy disks!
Intel 8086
  IBM-PC Used 8086
  16-bit registers
  1 MB addressable RAM (___-bit addressing)
  16-bit data bus
  Separate floating-point unit (8087)
  Backward-Compatibility: this approach allows older software programs (binary) to run on newer computers.

## Slide 86: The IBM-PC/AT
Intel 80286
  16-bit microprocessor registers
  16 MB addressable RAM (___-bit addressing)
  24-bit address bus
  Protected memory mode
  Several times faster than 8086
  Introduced IDE (Integrated Drive Electronics) BUS architecture
  Separate 80287 floating point unit (FPU)

## Slide 87: Intel IA-32 (32-Bit x86) Family
Intel386 (80386)
  32-bit data registers
  32-bit address, paging (virtual memory)
  __ GB addressable RAM
  Windows NT and Linux Operating System
Intel486
  Instruction pipelining
  FPU, inside the main chip
Pentium, +Pro, +II, +III, +4, +5
  32-bit address bus, 64-bit data
  Instruction superescalar

## Slide 88: IA-32 (32-Bit x86) Processor Architecture
Modes of operation
Basic execution environment
Floating-Point Unit FPU

## Slide 89: IA-32 Modes of Operation -1
Protected Mode
  native state for 80x86 CPUs (Windows NT, Linux)
  every resource can be used
    all the instructions, and devices
  4GB of central memory, 32-bit addresses
    the whole main memory
  programs (processes) given separate memory (processes) areas
  security: every process can not address other process area

## Slide 90: IA-32 Modes of Operation -2
Real-Address Mode
  implements programming environment of Intel 8086 processor
  1 MB of central memory, 20-bit addresses
    only 1 MB out of the 4GB
  native MS-DOS
  backward compatibility
    it runs on the 80x86 processor
  the MS-DOS works like a virtual machine
  program can cause MS-DOS crash
    None, the other Windows NT processes

## Slide 91: IA-32 Modes of Operation - 3
System Management Mode
  Provides OS with:
    boot configuration
    power management (power-on, battery level, shutdown)
    system security
    diagnostics
      main memory, disks unit, graphical cards, nic cards, mouse, keyboard, usb unit, monitors, …
    disks defragmenter
  This functions are implemented by computer (hardware) manufacturers

## Slide 92: IA-32 Modes of Operation - 4
Virtual-8086 sub-mode
  hybrid of Protected Mode
  allow several sessions of Real-Address Mode
  each session is a MS-DOS virtual machine
  each program has its own 8086 computer
  if a MS-DOS virtual machine crashes, it does not affect the other process
  every MS-DOS virtual machine uses 1 MB of the central memory

## Slide 93: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Agosto – diciembre 2022

## Slide 94: Basic Execution Environment
IA-32
Addressable memory
General-purpose registers
Index and base registers
Specialized register uses
Status flags

## Slide 95: IA-32 Addressable Memory
Protected mode
  4 GB
  32-bit address (0 - 4,294,967,295), 4-Byte address
Real-address mode and Virtual-8086 sub-mode
  1 MB space
  20-bit address (0 - 1,048,575), 2.5-Byte address
  In Protected Mode running multiple (Virtual-8086 sub mode) programs, each program has its own 1 MB memory area

## Slide 96: Protected Mode Memory

## Slide 97: Real-address Mode Memory

## Slide 98: Program Execution Registers
Named storage locations inside the CPU, optimized for high-speed.

## Slide 99: General-Purpose Registers (1/2)
32 bit-Registers: EAX, EBX, ECX, and EDX
Primarily used for arithmetic and data movement
Lower half of these registers can be broken down as:
  two 8-bit values, or / and
  one 16-bit value (both for backward-compatibility)

## Slide 100: General-Purpose Registers (2/2)
32 bit-Registers: ESI, EDI, EBP, and ESP
These registers are used for addressing
Lower half of these registers can be broken down as:
  one 16-bit value

## Slide 101: Some Specialized Register Uses (1 / 3)
32-bit General-Purpose Registers
  EAX – extended accumulator (mult, divi)
  ECX – CPU loop counter
  ESP – CPU extended stack pointer or SP
  ESI, EDI – index registers
  EBP – extended frame pointer (stack, for high-level languages parameters)
    Should not be used for arithmetic or data transfer

## Slide 102: Some Specialized Register Uses (2 / 3)
EIP – 32-bit Instruction Pointer (traditional PC, Program Counter)
  Contains address of next instruction to be executed
EFLAGS – 32-bit Processor Status Flags
  status and control flags
  each flag is a single binary bit
  A flag is set when it equals 1; it is clear (or reset) when it equals 0
  The flags are affected after exec instructions

## Slide 103: Status 1-bit Flags / EFLAGS
Carry
  unsigned arithmetic out of range
Overflow
  signed arithmetic out of range
Sign
  result is negative
Zero
  result is zero
Auxiliary Carry
  carry from bit 3 to bit 4, in 8-bit operand
Parity
  sum of 1 bits, is an even number (in LSB)

## Slide 104: Some Specialized Register Uses (3 / 3)
16-bit Segment Registers (for processes)
  CS – code segment, holds code; programs and procedures
  DS – data segment, contains most data used by a program
  SS – stack segment, defines the area of memory used for the stack
  ES, FS, GS - additional segments for extra data

## Slide 105: Process memory schema
0x00000000
0xFFFFFFFF
Memory address space
Code section
(text segment)
static data section
(data segment)
heap
(dynamic allocated mem)
stack
(storage call returns, etc.)
OS resources
(open files, network connect.,
Sound channels, …)
CPU
General Registers
PC
SP
EIP
ESP
CS >
DS >
SS >

## Slide 106: Memory Addressing Schemes
Lower address
Higher address
Lower address
Higher address
EXEC
FLOW
EXEC
FLOW

## Slide 107: Data allocation
32-bit Registers
  For 32-bit data values, signed or not.
  MSB: bit 31; LSB bit 0.
8-bit Memory Locations
  How come a 32-bit value is allocated in 8-bit memory locations?

## Slide 108: 1- Byte Data allocation
1-Byte Example, AL register and byte variable alfa:
AL: containing a numerical value of 12h
alfa, has a memory address location of 000001002

## Slide 109: Endianness memory storage
Is the sequential order in which Bytes (more than one), representing a numerical value, are stored in main memory.
  Numerical value storage > 1 Byte
Two formats for Endianness
  Big-endian, MSB stored first, … LSB stored last
  Little-endian, LSB stored first, … MSB stored last

## Slide 110: Little Endian Order
2-Byte Example, BX register and short variable beta:
BX: containing a numerical value of 1234h
beta, has a memory address location of 000001002

## Slide 111: Little Endian Order
4-Byte Example, ECX register and integer variable delta:
ECX: containing a numerical value of 12345678h
delta, has a memory address location of 000001002

## Slide 112: 64-bit x86-64 Processors - 1
Intel64 (x86-64 specification)
  P6 series, extended to 64 GB (___-bit addressing)
  64-bit linear address space
  64-bit Mode, Windows 64 uses this
  Protected, Real-address and System Management Modes.
IA-32e Mode (backward-compatibility) has two sub-modes
  Compatibility Mode for legacy 16- and 32-bit applications, Windows supports only 32-bit apps in this mode
  64-bit Mode uses 64-bit addresses and 64-bit (and 32-bit) operands

## Slide 113: 64-bit x86-64 Processors - 2
64-bit Operating Systems over x86-64 Processors
E.g. Windows v7, v10, servers v2012, …
  What exec programs are installed inside the next folders and Why Are these folders Split Up?:
    “C:\Program Files”? ________
    “C:\Program Files (x86)” ? ________
  Task Manager display it up > (32 bits)

## Slide 114: 64-bit x86-64 Processors
Basic Execution Environment
  addresses can be 64 bits
  16 64-bit general purpose registers RAX-R15
  A 64-bit status flags named RFLAGS
  64-bit instruction pointer (Program Counter) named RIP

## Slide 115: 64-Bit General Purpose Registers
64-bit general purpose registers:
  RAX, RBX, RCX, RDX, RDI, RSI, RBP, RSP, R8-R15
32-bit general purpose registers:
  EAX, EBX, ECX, EDX, EDI, ESI, EBP, ESP, R8D-R15D
16-bit general purpose registers:
  AX, BX, CX, DX, DI, SI, BP, SP, R8W-R15W
8-bit general purpose registers:
  AL, BL, CL, DL, AH, BH, CH, DH, R8B-R15B

## Slide 116: 64-Bit Registers RAX-R15

## Slide 117: 64-Bit Registers RFLAGS, RIP

## Slide 118: Multipurpose Registers - 1
RAX - a 64-bit register (RAX), a 32-bit register (accumulator) (EAX), a 16-bit register (AX), or as either of two 8-bit registers (AH and AL).
The accumulator is used for instructions such as multiplication, division, and some of the adjustment instructions.
RBX, addressable as RBX, EBX, BX, BH, BL.
  BX register (base index) sometimes holds offset address of a location in the memory system in all versions of the microprocessor

## Slide 119: Multipurpose Registers - 2
RCX, as RCX, ECX, CX, CH, or CL.
  a (count) general-purpose register that also holds the count for various instructions
RDX, as RDX, EDX, DX, DH, or DL.
  a (data) general-purpose register
  holds a part of the result from a multiplication or part of dividend before a division
RBP, as RBP, EBP, or BP.
  points to a memory (base pointer) location for memory data transfers

## Slide 120: Multipurpose Registers - 3
R8 - R15.
  data are addressed as 64-, 32-, 16-, or 8-bit sizes and are of general purpose
  bits 8 to 15 are not directly addressable as a byte

## Slide 121: Multipurpose Registers - 4
RDI addressable as RDI, EDI, or DI.
  often addresses (destination index) string destination data for the string instructions
RSI used as RSI, ESI, or SI.
  the (source index) register addresses source string data for the string instructions
  like RDI, RSI also functions as a general- purpose register

## Slide 122: Special-Purpose Registers
RIP addresses the next instruction in a section of memory.
  defined as (instruction pointer) a code segment
RSP addresses an area of memory called the stack.
  the (stack pointer) stores data through this pointer
RFLAGS indicate the condition of the microprocessor and control its operation.

## Slide 123: Little Endian Order
8-Byte Example, RAX register and integer*8 variable omega:
RAX: containing a numerical value of D9B356341278A2AFh
omega, has a memory address location of 000001002

## Slide 124: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Chapters: Brey, Barry B., The Intel Microprocessors
Notas de Ramón Ríos.
Agosto – diciembre 2022

## Slide 125: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 126: Assembly Language vs High-Level L
Assembly
One phrase per line
One instruction per line
Operations (+,-,*,/,…) are represented by mnemonics (representing instructions).
Is not structured
Very short object programs
Runs faster

## Slide 127: Example Program
;Add two numbers and displays the result
.CODE
main PROC
mov eax, 24 ; move 24 to the EAX register
add eax, 17 ; add 17 to the EAX register
call WriteInt ; display EAX content value
exit ; to end execution
main END
;”.CODE”, ”main”: directives of MASM
;”WriteInt”: function of the Library Subroutine of MASM (Assembler)
;”exit”: function of Windows; translated to “call exit”

## Slide 128: Ejecución de Programas en Leng. Ensamblador
Flujo tradicional para desarrollar y correr programas en Leng. Ensamblador (Assembly):
  Ensamble con el Ensamblador (Assembler), prog.asm a prog.obj
  Ligado o vinculado (linking) con el Linker, prog.obj a prog.exe
  Ejecución de programa prog.exe
prog.asm
Ensamblador
prog.obj
prog.exe
Linker
Programa fuente
Programa objeto
Programa ejecutable

## Slide 129: Basic Elements of Assembly Language
Integer constants
Integer expressions
Character and string constants
Identifiers and Reserved words
Directives
Mnemonics and Operands for instructions
Labels
Comments

## Slide 130: Integer Constants
[{+ | -}] digits [radix]
Optional leading + or – sign, default +
Radix: Binary, decimal, hexadecimal, or octal digits
Common radix characters:
  h – hexadecimal
  q | o – octal
  d – decimal (default)
  b – binary
  r – encoded real
  t – decimal (alternate)
  y – binary (alternate)
If no radix given, assumed to be decimal
Examples: 30d, 30, 6Ah, -42, 1101b, 53o
Hexadecimal beginning with letter, prefix 0 (zero): 0B4h, 0A5h ;Why?

## Slide 131: Real Number Constants -1
Represented as decimal reals or encoded (hexadecimal) reals
Decimal real contains optional sign followed by integer, decimal point, and optional integer that expresses a fractional and an optional exponent
  [sign] integer.[integer] [exponent]
  Sign {+, -}
  Exponent E[{+, -}] integer
Examples
  2.
  +3.0
  -44.2E+05
  26.E5

## Slide 132: Real Number Constants -2
Represented as decimal encoded (hexadecimal) reals
Example
  Binary representation of +1.0
  0011 1111 1000 0000 0000 0000 0000 0000b
Example
  Decimal encoded hexadecimal real of +1.0
  3F800000r

## Slide 133: Character and String Constants
Enclose character in single or double quotes
  'A', "x"
  ASCII character = 1 byte
Enclose strings in single or double quotes
  "ABC"
  'xyz'
  Each character occupies a single byte
Embedded quotes:
  'Say "Goodnight," Gracias'

## Slide 134: Character and String Constants
.DATA
Alfa SDWORD 7 ; allocate a signed 4-Byte memory
Beta SDWORD 11h ; 11h > 17
R SDWORD 0
msgr BYTE "El Resultado R= ", 0 ; bytes allocated?
.CODE
main PROC
mov EAX, Alfa ; EAX:7
neg EAX ; -? EAX: -7
add EAX, 9 ; -? EAX: 2
sub EAX, Beta ; -? EAX: -15
inc EAX ; -? EAX: -14
mov R, EAX ; R = resultado -?
mov EDX, OFFSET msgr
call WriteString ; imprime el String que comienza en msgr
call WriteInt ;imprime el contenido de EAX, o sea de R
exit
main ENDP
END main

## Slide 135: Identifiers
Identifiers
  Programmer-chosen name to identify a variable, constant, procedure (function), or label
  1-247 characters, including digits
  not case sensitive
  first character must be a letter, _, @, ?, or $
    Subsequent characters may also be digits
  Cannot be the same as a reserved word
  @ is used by assembler as a prefix for predefined symbols, so avoid it identifiers
Examples
  var1, Count, $first, _hello, MAX,
  open_file, myFile, xVal, _12345

## Slide 136: Reserved Words
Reserved words cannot be used as identifiers
  Instruction mnemonics
    MOV, ADD, MUL,, …
  Register names
    EAX, EBX, …
  Directives –
    .data, .code, .stack
    PROC, END
    BYTE, WORD, SDWORD
See MASM reference in Appendix A; Irvine

## Slide 137: Directives 1
Commands embedded in the source code that are recognized and acted upon by the Assembler,
  Not part of the Intel instruction set
  tells MASM how to assemble programs
  Work at assembly time
  Do not execute (.exe) at runtime

## Slide 138: Directives 2
Commands . . .
  Used to declare code, data areas, select memory model, declare procedures, etc.
    .code, .data, .DATA, .Data, .stack
    flat
    PROC, END
    Type attributes – provides size and usage information
      BYTE, WORD, DWORD, SDWORD
one DWORD 34 ; DWORD directive, set aside
; enough space for double word
mov eax, one ; MOV instruction

## Slide 139: Instructions
An instruction is a statement that becomes executable when after a program is assembled.
Assembled into machine code ( 0s and 1s ) by assembler
Loaded and executed at runtime by the CPU
We use the Intel IA-32/64 instruction set
An instruction contains four basic parts:
  Label (optional)
  Mnemonic (required)
  Operand (depends on the instruction)
  Comment (optional)
Basic syntax
  [ label[:] ] [ mnemonic [operands] ] [ ; comment ] ?

## Slide 140: Labels
Act as place markers or addresses
  marks the address (offset) of code and data
Follow identifier rules
Data label
  must be unique
  example: temp (not followed by colon)
  temp DWORD 100
Code label
  target of some type of jump
  example: here: (followed by colon)
here:
mov ebx, temp
…
jmp here

## Slide 141: Mnemonics and Operands
Instruction Mnemonics
  short word that identifies an instruction
  examples: MOV, ADD, SUB, MUL, INC, DEC, NOP, JUMP, CALL, IMUL
  describe the type of operation
Operands
  each instruction can have between 0 and tree operands
  constant 96
  constant expression 4+5*2 ; in the Assembly time 14
  register EAX
  memory (data label) temp ; variable alike temp+2
Constants and constant expressions are often called immediate values (at assembly time)

## Slide 142: Mnemonics and Operands Examples
STC instruction
stc ; set Carry flag
INC instruction
inc eax ; add 1 to EAX
MOV instruction
mov temp, ebx ; move EBX to temp
; first operation is destination
; second is the source
IMUL instruction (three operands)
imul eax, ebx, 5 ; EBX multiplied by 5, product in EAX

## Slide 143: Comments 1
Comments are good!
  explain the program's purpose
  when it was written, and by whom
  revision information
  Technical notes about coding (programming) techniques
  application-specific explanations
Single-line comments
  begin with semicolon (;)
Multi-line comments
  begin with COMMENT directive and a programmer-chosen character
  end with the same programmer-chosen character

## Slide 144: Comments 2
Single line comment
  inc eax ; single line at end of instruction
  ; single line at beginning of line
Multiline comment
COMMENT !
This line is a comment
This line is also a comment
!
COMMENT &
This is a comment
This is also a comment
&

## Slide 145: NOP instruction
Doesn’t do anything, just waste a clock cycle (tick)
Takes up one byte of memory
Sometimes used by compilers and assemblers to align code to even-address boundaries. (as file blocks)
The following MOV generates three machine code bytes. The NOP aligns the address of the third instruction to a doubleword boundary (even multiple of 4)
00000000 66 8B C3 mov ax, bx
00000003 90 nop ; align next instruction
00000004

## Slide 146: Instruction Format Examples
No operands
  stc, nop ; set Carry flag, no operation
One operand
  mul 7 ; constant
  inc temp ; memory
Two operands
  add ebx, ecx ; register, register
  sub temp, 25 ; memory, constant
  add eax, 36*25 ; register, constant-expression

## Slide 147: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Agosto – diciembre 2022

## Slide 148: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 149: IA Directives: Defining Data
DATA SECTION (.data, .DATA) in 32-bit programs
Intrinsic Data Types
Data Definition Statement
Defining BYTE and SBYTE Data
Following the Little-Endian Order
Defining WORD and SWORD Data
Defining DWORD and SDWORD Data
Defining QWORD Data
Defining TBYTE Data
Defining Real Number Data
Declaring Uninitialized Data

## Slide 150: IA Directives: Defining Data
These Assembly Directives in DATA SECTION:
  Allocate memory space (bytes), and
  Can define an initial value in the memory space.
.DATA / .data section:
  Fixes the initial address of the user program (.asm file).

## Slide 151: Directives of Intrinsic Data Types 1
INTEGERs: size and content (unsigned, signed)
BYTE, SBYTE
  8-bit unsigned integer; 8-bit signed integer (1 byte)
WORD, SWORD
  16-bit unsigned & signed integer (2 bytes)
DWORD, SDWORD
  32-bit unsigned & signed integer (Double word, 4 bytes)
QWORD, SQWORD
  64-bit unsigned integer (Quad word, 8 bytes)
  64-bit signed integer (not valid in IA-32)
TBYTE
  80-bit integer (Ten bytes)

## Slide 152: Directives of Intrinsic Data Types 2
REALs, with fractions
REAL4
  4-byte IEEE short real
REAL8
  8-byte IEEE long real
REAL10
  10-byte IEEE extended real

## Slide 153: Data Definition Statement
A data definition statement (a directive) sets aside storage in memory for a variable.
May optionally assign a name (data label) to the data
Syntax:
  [name] directive initializer [,initializer] . . .
  alfa BYTE 10
All initializers become binary data in memory

## Slide 154: Defining BYTE and SBYTE Data
beta BYTE 'A' ; character constant
gamma BYTE 0 ; smallest unsigned byte
omega BYTE 255 ; largest unsigned byte
delta SBYTE -128 ; smallest signed byte
sigma SBYTE +127 ; largest signed byte
eagle BYTE ? ; uninitialized byte
falcon BYTE 10h
Each of the following defines a single byte of storage:

## Slide 155: Defining Multiple Initializers
list1 BYTE 10,20h,30,40h
list2 BYTE 10h,20,30h,40h
BYTE 50h,60h,70h,80h
BYTE 81,82h,83h,84h
list3 BYTE ?,32,41h,00100010b
list4 BYTE 0Ah,20h,‘A’,22h
Offset = relative address
Examples that use multiple initializers:
list2
Offset | Value (h)
0000 | 0A
0001 | 20
0002 | 1E
0003 | 40
0004 | 10
0005 | 14
0006 | 30
0007 | 40
0008 | 50
0009 | 60
000A | 70
000B | 80
000C | 51
000D | 82
000E | 83
000F | 84
0010 | ?
list1
list3

## Slide 156: Defining Strings 1
A string is implemented as an array of characters
  For convenience, it is usually enclosed in quotation marks
  For HLL It will be null-terminated (ending with ,0)
Examples:
str1 BYTE "Enter your name",0
str2 BYTE 'Error: halting program',0
str3 BYTE 'A','E','I','O','U’
AEQuote BYTE "Imgination is more important than "
BYTE “knowledge, by Albert Einstein.",0

## Slide 157: Defining Strings 2
New-Line characters sequence (HLL: “\n”):
  0Dh = carriage return (End-of-Line)
  0Ah = line feed (Next-Line)
; HLL “\n” example:
; String str4= “Name*\n” +
; “Enter: “;
str4 BYTE “Name*",0Dh,0Ah
BYTE “Enter: ",0
Idea: Define all strings used by your program in the same area of the data segment.

## Slide 158: Using the DUP Operator
Use DUP to allocate (create space for) an array or string. Syntax: counter DUP ( argument )
Counter and argument must be constants or constant expressions
v1 BYTE 20 DUP(0) ; 20 bytes, all with zero
v2 BYTE 20 DUP(?) ; 20 bytes, uninitialized
v3 BYTE 4 DUP("STACK") ; 20 bytes: "STACKSTACKSTACKSTACK"
v4 BYTE 10h,3 DUP(0),20 ; 5 bytes
10h
00
00
00
14h
v4

## Slide 159: Little Endian Order
All data types larger than one byte, store their individual bytes in reverse order. The least significant byte occurs at the first (lowest) memory address.
2-Byte Example:
val1 WORD 1234h
0000 0000: | 34
0000 0001: | 12

## Slide 160: Defining WORD and SWORD Data
Define storage for 16-bit integers
  or double characters
  single value or multiple values
word1 WORD 65535 ; largest unsigned value
word2 SWORD –32768 ; smallest signed value
word3 WORD ? ; uninitialized, unsigned
word4 WORD "AB" ; double characters
myList WORD 1,2,5 ; array of words
array WORD 5 DUP(25h) ; uninitialized array

## Slide 161: Little Endian Order
4-Byte Example:
val2 DWORD 12345678h
0000 0000: | 78
0000 0001: | 56
0000 0002: | 34
0000 0003: | 12

## Slide 162: Defining DWORD and SDWORD Data
val2 DWORD 12345678h ; unsigned
val3 SDWORD –2147483648 ; signed
val4 SDWORD –3, 2 ; signed array
val5 DWORD “ABCD” ; quad characters
pVal DWORD val4 ;What´s going on here?
val6 DWORD 20 DUP(?) ; unsigned array
Storage definitions for signed and unsigned 32-bit integers (4 bytes):

## Slide 163: Defining QWORD, TBYTE, Real Data
quad1 QWORD 123456789ABCDEF0h ;____ Bytes?
val1 TBYTE 102030405060708090A0h
rVal1 REAL4 -2.1
rVal2 REAL8 3.2E-260
rVal3 REAL10 4.6E+4096
ShortArray REAL4 20 DUP(0.0)
Storage definitions for quadwords, tenbyte values, and real numbers:

## Slide 164: Adding Variables to AddSub
TITLE Add and Subtract, Version 2 (AddSub2.asm)
; This program adds and subtracts 32-bit unsigned
; integers and stores the sum in a variable.
INCLUDE Irvine32.inc
.DATA
sal1 DWORD 10000h
sal2 DWORD 40000h
sal3 DWORD 20000h
finalVal DWORD ?
.CODE
main PROC
MOV EAX,sal1 ; EAX ?
  ADD EAX,sal2 ; EAX ?
  SUB EAX,sal3 ; EAX ?
  MOV finalVal,EAX ; store the result (_____?)
  CALL DumpRegs ; display the registers
  EXIT
main ENDP
END main

## Slide 165: Two-pass Assembler
When Assembling, the Assembler parses twice the source code of Assembly program (.asm).
  PASS-1: Define identifiers (e.g. labels), allocate each one with a memory address, and remember them in a Symbol Table.
  PASS-2: Generate object code (.obj), by converting instructions (nmonics and operands), into respective machine language (binary).

## Slide 166: OFFSET Operator Directive
OFFSET works like part of one operand in an instruction (CODE segment)
OFFSET returns the distance, in bytes, between the address of a LABEL and the beginning of its enclosing DATA segment
  Protected mode: 32, 64 bits
  Real mode: 16 bits

## Slide 167: OFFSET Examples
.DATA
BYTE 404000h DUP(?)
bVal BYTE 3
wVal WORD 7
dVal DWORD 4
dVal2 DWORD 5
.CODE
MOV ESI,OFFSET bVal ; ESI = 00______
MOV ESI,OFFSET wVal ; ESI = 00______
MOV ESI,OFFSET dVal ; ESI = 00______
MOV ESI,OFFSET dVal2 ; ESI = 00______

## Slide 168: Relating to C/C++
// C++ version:
char array[1000];
char * p = array;
The value returned by OFFSET is a pointer. Compare the following code written for both C++ and assembly language:
; Assembly language:
.DATA
array BYTE 1000 DUP(?)
p DWORD ?
.CODE
MOV ESI,OFFSET array
MOV p, ESI

## Slide 169: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Agosto – diciembre 2022

## Slide 170: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 171: Instruction Format
x86 instruction format
    [label:] [mnemonic [operands]] [;comments]
mnemonic [operands]
    mnemonic
    mnemonic source
    mnemonic destination
    mnemonic destination, source
    mnemonic destination, source-1 , source-2

## Slide 172: Operand Types
Imm-ediate – a constant integer (8, 16, or 32 bits)
  value is encoded within the instruction
Reg-ister – the name of a register (8, 16, or 32 bits)
  register name is converted to a number and encoded within the instruction
Mem-ory – reference to a location in memory (8, 16, or 32 bits)
  memory address is encoded within the instruction, or a register holds the address of a memory location

## Slide 173: Instruction Operand Notation

## Slide 174: Instruction Set
Data Transfer Instruction
MOV
( HLL = )

## Slide 175: MOV Instruction
Move from source operand to destination operand.
Syntax:
    MOV destination, source
    ; HLL, destination=source

## Slide 176: General Operand-Variants of MOV
MOV reg, reg
MOV mem, reg
MOV reg, mem
MOV mem, imm
MOV reg, imm
No more than one memory operand permitted

## Slide 177: Direct Memory Operands
A direct memory operand is a named reference to storage in memory
The named reference (label) is automatically dereferenced by the assembler
.DATA
var1 BYTE 10h
.CODE
MOV EAX,21h ; EAX = 00000021h
MOV ECX,EAX ; ECX = 00000021h
MOV AL,var1 ; AL = 10h
MOV AL,[var1] ; AL = 10h

## Slide 178: MOV Instruction 1
.DATA
count BYTE 100
wVal WORD 2
.CODE
MOV BL,count ; ?
MOV AX,wVal ; ?
MOV count,AL ; ?
MOV AL,wVal ; ?
MOV AX,count ; ?
MOV EAX,count ; ?
Explain why each of the following MOV statements are valid or invalid:

## Slide 179: MOV Instruction 2
.DATA
bVal BYTE 100
bVal2 BYTE ?
wVal WORD 2
dVal DWORD 5
.CODE
MOV DS,45 ?
MOV ESI,wVal ?
MOV EIP,dVal ?
MOV 25,bVal ?
MOV bVal2,bVal ?
CS, EIP, and IP cannot be the destination
No immediate to segment moves
Explain why each of the following MOV statements are valid or invalid:

## Slide 180: Direct-Offset Operands 1
.DATA
arrayB BYTE 10h,20h,30h,40h
.CODE
MOV AL,arrayB+1 ; AL = 20h
MOV AL,[arrayB+1] ; alternative notation
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.
Q: Why doesn't arrayB+1 produce 11h?

## Slide 181: Direct-Offset Operands 2
.DATA
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.CODE
MOV AX,[arrayW+2] ; AX = 2000h
MOV AX,[arrayW+4] ; AX = 3000h
MOV EAX,[arrayD+4] ; EAX = 00000002h
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.
; Will the following statements assemble?
MOV AX,[arrayW-2] ; ??
MOV EAX,[arrayD+16] ; ??
What will happen when they run?

## Slide 182: ADD and SUB Instructions
ADD, syntax:
    ADD destination, source
    ; HLL, destination= destination+source
SUB, syntax:
    SUB destination, source
    ; HLL, destination= destination-source

## Slide 183: Two operand instructions ADD, SUB
ADD reg, reg SUB reg, reg
ADD mem, reg SUB mem, reg
ADD reg, mem SUB reg, mem
ADD mem, imm SUB mem, imm
ADD reg, imm SUB reg, imm

## Slide 184: INC and DEC Instructions
INC, syntax:
    INC destination
    ; HLL, destination= destination+1
DEC, syntax:
    DEC destination
    ; HLL, destination= destination-1

## Slide 185: One operand instructions INC, DEC
INC reg DEC reg
INC mem DEC mem

## Slide 186: Addressing in Operands
Direct Addressing
  Register
  Memory
  Immediate
And many more Addressing …

## Slide 187: Instruction Set
Assembly Language of x86 Processors
Appendix B
The x86 Instruction Set.

## Slide 188: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Agosto - diciembre, 2022

## Slide 189: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 190: Machine Language
Native binary code microprocessor instructions vary in length from 1 to 13 Bytes
Over 100,000 variations of machine language instructions. There is no complete list of these variations
Some bits in a machine language instruction are given (opcode); remaining bits are determined for each variation of the instruction.

## Slide 191: Instruction Formats
In the Real mode (DOS over 8086), 80386 and above assume all instructions are 16-bit mode instructions.
In Protected mode (Windows & Linux), the upper byte of the descriptor contains the bit that selects either the 16- or 32-bit instruction mode

## Slide 192: Opcode field, Byte 1
Identifies the operation (mov, add, sub, …).
Either 1 or 2 bytes long for instructions.
Binary Opcode: first 6 bits of the first byte.
D bit, indicates the direction of the data flow:
  Into or From, a Register
W bit indicates whether the data are a byte or a word

## Slide 193: 32-bit instruction examples (1)
ASSEMBLY MEMORY ALLOCATION
NOP ;1 Byte
  1st Byte: Opcode&D&W

## Slide 194: [ Opcode field, Byte 2 ]
MOD field: addressing mode code
REG field:
  register code, destination/source operand
R/M field:
  Register, memory or immediate operand
  If register: register code, source
  If memory: code and address, destination/source
  If immediate: code and data, source

## Slide 195: 32-bit instruction examples (1)
ASSEMBLY MEMORY ALLOCATION
NOP ;1 Byte
  1st Byte: Opcode&D&W
INC EAX ;2 Bytes
  1st Byte: Opcode&D&W
  2nd Byte: MOD&REG&R/M

## Slide 196: Instruction: [ Bytes 3, 4, … ]
These Bytes exist when R/M field is:
  a Memory operand (Displacement, Offset), or
  an Immediate operand

## Slide 197: 32-bit instruction examples (3)
ASSEMBLY MEMORY ALLOCATION
MOV alfa, EBX ;6 Bytes
  1st Byte: Opcode&D&W
  2nd Byte: MOD&REG&R/M
  3rd, 4th, 5th, 6th Bytes: memory address of alfa

## Slide 198: 32-bit instruction examples (3)
ASSEMBLY MEMORY ALLOCATION
MOV ECX, EDX ; Bytes? ___
  1st Byte: Opcode&D&W
  2nd Byte: MOD&REG&R/M
  ?
MOV alfa, 34h ; Bytes? ___
  1st Byte: Opcode&D&W
  2nd Byte: MOD&REG&R/M
  ?

## Slide 199: Referencias
Chapters: Brey, Barry B., The Intel Microprocessors.
Notas de Ramón Ríos.
Agosto – diciembre, 2022

## Slide 200: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 201: Instruction Set
Data Transfer Instructions (cont…)
Besides MOV

## Slide 202: Zero Extension
MOV BL,10001111b
MOVZX AX,BL ; zero-extension
When you copy a smaller value into a larger destination, the MOVZX instruction fills (extends) the upper half of the destination with zeros.
The destination must be a register.

## Slide 203: General Variants of MOVZX
MOVZX reg32, reg/mem8
MOVZX reg32, reg/mem16
MOVZX reg16, reg/mem8

## Slide 204: MOVZX with EAX register
CALL DumpRegs
MOV BL,10001111b ; chart Zero Extension BL=__h
MOVZX EAX,BL ; showing MOVZX with EAX register
CALL DumpRegs

## Slide 205: Sign Extension
MOV BL,10001111b
MOVSX AX,BL ; sign extension
The MOVSX instruction fills the upper half of the destination with a copy of the source operand's sign bit.
The destination must be a register.

## Slide 206: General Variants of MOVSX
MOVSX reg32, reg/mem8
MOVSX reg32, reg/mem16
MOVSX reg16, reg/mem8

## Slide 207: XCHG Instruction
.DATA
var1 WORD 1000h
var2 WORD 2000h
.CODE
; EAX contains 12345678h, EBX has ABCDEF01h.
XCHG var1,BX ; var1=____h, BX=____h, EBX=________h
XCHG EAX,EBX ; EAX=________, EBX=________
XCHG AX,BX ; AX=____, BX=____
XCHG AH,AL ; AH=__, AL=____
XCHG var1,var2 ; var1=____h, var2=____h
XCHG exchanges the values of two operands. At least one operand must be a register. No immediate operands are permitted.

## Slide 208: General Variants of XCHG
XCHG reg, reg
XCHG reg, mem
XCHG mem, reg

## Slide 209: Your turn. . .
Write a program that rearranges the values of three doubleword values in the following array as: 3, 1, 2.
  .data
  arrayD DWORD 1,2,3
  .code
Step 2:
Step1:
MOV EAX, arrayD
XCHG . . .
XCHG . . .
MOV . . .

## Slide 210: XCHG Example
; xchg examples
CALL DumpRegs
MOV EAX, arrayD
XCHG EAX, [arrayD+4]
XCHG EAX, [arrayD+8]
MOV arrayD, EAX
. . .
MOV EAX, [arrayD]
MOV EBX, [arrayD+4]
MOV ECX, [arrayD+8]
CALL DumpRegs

## Slide 211: Evaluate this . . .
.data
myBytes BYTE 80h,66h,0A5h
How about the following code. Is anything missing?
; EAX has 00A5668Bh, EBX has 7EFDE08Fh
MOVZX AX, myBytes
MOV BL,[myBytes+1]
ADD AX, BX
MOV BL,[myBytes+2]
ADD AX, BX ; AX = ?

## Slide 212: Evaluate this . . . (cont)
CALL DumpRegs
; MOVZX examples EAX: 00A5668Bh, EBX: 7EFDE08Fh
MOVZX AX, myBytes ; EAX: 00A50080h
MOV BL, [myBytes+1] ; EBX: 7EFDE066h
ADD AX, BX ; EAX: 00A5E0E6h
MOV BL, [myBytes+2] ; EBX: 7EFDE0A5h
ADD AX, BX ; AX = EAX: 00A5C18Bh
CALL DumpRegs

## Slide 213: Evaluate this . . . (cont)
CALL DumpRegs
; MOVZX examples EAX: 00A5668Bh, EBX: 7EFDE08Fh
MOVZX AX,myBytes ; EAX: 00A50080h
MOV BX,0 ; EBX: 7EFD0000h
MOV BL,[myBytes+1] ; EBX: 7EFD0066h
ADD AX,BX ; EAX: 00A500E6h
MOV BL,[myBytes+2] ; EBX: 7EFD00A5h
ADD AX,BX ; AX = EAX: 00A5018Bh
CALL DumpRegs

## Slide 214: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
Agosto – diciembre, 2022

## Slide 215: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 216: Instruction Set
Addition and Subtraction
add, sub, inc, dec, neg

## Slide 217: ADD and SUB Instructions
ADD destination, source
  destination  destination + source
SUB destination, source
  destination  destination – source
Same operand rules as for the MOV instruction

## Slide 218: Two operand instructions ADD, SUB
ADD reg, reg SUB reg, reg
ADD mem, reg SUB mem, reg
ADD reg, mem SUB reg, mem
ADD mem, imm SUB mem, imm
ADD reg, imm SUB reg, imm

## Slide 219: ADD and SUB Examples
.DATA
var1 DWORD 10000h
var2 DWORD 20000h
.CODE ; ---EAX(0000h,AX)
MOV EAX, var1 ; ________ h
ADD EAX, var2 ; ________ h
ADD AX, 0FFFFh ; ________ h
ADD EAX, 1 ; ________ h
SUB AX, 1 ; ________ h

## Slide 220: INC and DEC Instructions
Add 1, Subtract 1 from destination operand
  operand may be register or memory
INC destination
    destination  destination + 1
DEC destination
    destination  destination – 1

## Slide 221: One operand instructions INC, DEC
INC reg INC mem
DEC reg DEC mem

## Slide 222: INC and DEC Examples
.DATA
myWord WORD 1000h
myDword DWORD 10000000h
.CODE
INC myWord ; ________ h
DEC myWord ; ________ h
INC myDword ; ________ h
MOV AX, 00FFh ; AX= ____ h
INC AX ; AX= ____ h
MOV AX, 00FFh ; AX= ____ h
INC AL ; AL= __h AX= ____ h

## Slide 223: Your turn...
Show the value of the destination operand after each of the following instructions executes:
.DATA
myByte BYTE 0FFh, 0
.CODE
MOV AL, myByte ; AL= __h
MOV AH,[myByte+1] ; AH= __h, AX= ____h
DEC AH ; AH= __h, AX= ____h
INC AL ; AL= __h, AX= ____h
DEC AX ; AX= ____h

## Slide 224: One operand instruction NEG
NEG reg NEG mem

## Slide 225: NEG (negate) Instruction
.DATA
valB SBYTE 1,0
valC SBYTE -128
.CODE
NEG valB ; valB = ________
NEG [valB + 1] ; valB+1 = ________
NEG valC ; valC = ________
The processor implements NEG operand using the following internal operation:
operand = 0 - operand
Two’s complement operation.

## Slide 226: NEG (negate) Instruction
.DATA
valB SBYTE -1
valW SWORD +32767
.CODE
MOV AL, valB ; AL = ____
NEG AL ; AL = ____
NEG valW ; valW = ________
Reverses the sign of an operand. Operand can be a register or memory operand.
Suppose AX contains –32,768 and we apply NEG to it. Will the result be valid?

## Slide 227: Implementing Arithmetic Expressions
.DATA
Rval DWORD ?
Xval DWORD 26
Yval DWORD 30
Zval DWORD 40
.CODE
MOV . . .
High Level Languages compilers translate mathematical expressions into assembly language. Recall precedence order.
For example:
Rval = -Xval + (Yval – Zval)
Do not modify Xval, Yval and Zval contents.

## Slide 228: Your turn...
MOV ...
Translate the following expression into assembly language. Do not permit Xval, Yval, or Zval to be modified:
Rval = Xval - (-Yval + Zval)
Assume that all values are signed doublewords.

## Slide 229: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos
Ago-Dic 2022

## Slide 230: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 231: HLL Structured instructions. via
Algorithm ---- program
Structured thinking
Algorithm structures
    SELECTIVES: If-then, if-then-else, switch-case
    REPETITIVES: while, for, do-while, repeat
There are not such instructions in machine language.
The programmer must do the implementation.

## Slide 232: Flags Affected by Arithmetic
The CPU has a number of Status Flags that reflect the outcome of arithmetic and bitwise operations (machine instructions)
  based on the contents of the destination operand
  Instructions ADD, CLC, CMP, DEC, INC, IMUL, NEG, TEST, and many more . . . except MOV (*)
Essential flags:
  ZeroF ZF, SignF SF, CarryF CF, OverflowF OF, AxiliaryF AF, ParityF PF
(*)The MOV instruction never affects the flags.

## Slide 233: Status Flags - Review iVc
The Zero flag ZF is set when the destination (result) equals zero.
The Carry flag CF is set when a result that is too large (or too small) for the destination; unsigned out-of-range result value.
The Sign flag SF is set if the destination is negative, otherwise it is clear. A Signed result value.
The Overflow flag OF is set when a destination is a signed out-of-range result value.
The Auxiliary Carry flag AF is set when an operation produces a carry out from bit 3 to bit 4.
The Parity flag PF is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.
CONDITIONAL JUMPS WILL USE THESE FLAGS

## Slide 234: Conditional Jumps
Conditional Jump instructions jump if
  a flag is on (1),
  a flag is off (0),
  some flags are on; or
  some flags are off.

## Slide 235: CPU flags affected
Assembly Language for x86 Processors Book
  Appendix B. The x86 Instruction Set

## Slide 236: 16-bit FLAGS register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | nt | iop | iop | OF | df | if | tf | SF | ZF | 0 | AF | 0 | PF | 1 | CF
FLAGS categories
STATUS flags: OF, SF, ZF, AF, PF, CF
CONTROL flags: tf, if, df
SYSTEM flags: iop, nt
Reserved bits: 0s and 1.

## Slide 237: 32-bit EFLAGS register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | nt | iop | iop | OF | df | if | tf | SF | ZF | 0 | AF | 0 | PF | 1 | CF
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | id | vip | vif | ac | vm | rf
FLAGS categories
STATUS flags: OF, SF, ZF, AF, PF, CF
CONTROL flags: tf, if, df
SYSTEM flags: iop, nt, rf, vm, ac, vif, vip, id
Reserved bits: 0s and 1.

## Slide 238: 64-bit RFLAGS register
63 | 62 | 61 | 60 | 59 | 58 | 57 | 56 | 54 | 54 | 53 | 52 | 51 | 50 | 49 | 48
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | nt | iop | iop | OF | df | if | tf | SF | ZF | 0 | AF | 0 | PF | 1 | CF
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | id | vip | vif | ac | vm | rf
47 | 46 | 45 | 44 | 43 | 42 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 34 | 33 | 32
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 239: CPU Conceptual Map
status flags
ALU
conditional jumps
branching logic
arithmetic & bitwise operations
part of
used by
provide
attached to
affect
CU
executes next
executes

## Slide 240: Signed and Unsigned Integers
A CPU Hardware Viewpoint
All CPU instructions operate exactly the same on signed and unsigned integers
The CPU cannot distinguish between signed and unsigned integers
YOU, the PROGRAMMER, are solely responsible for using the correct data type with each instruction

## Slide 241: ZERO Flag (ZF)
MOV CX,1 ; none flag is changed
SUB CX,1 ; CX= 0, ZF= 1, CF= __
MOV AX,0FFFFh
INC AX ; AX= 0, ZF= 1 , CF= __
INC AX ; AX= 1, ZF= 0 , CF= __
The ZERO flag is set when the result of an operation produces zero in the destination operand.
Remember...
A flag is set when it equals 1.
A flag is clear when it equals 0.

## Slide 242: CARRY Flag (CF)
The CARRY flag is set when the result of an operation generates an unsigned value that is out of range (too big or too small for the destination operand).
MOV AL,0FFh
ADD AL,1 ; CF= 1, AL= 00, ZF= __
; Try to go below zero:
MOV AL,0
SUB AL,1 ; CF= 1, AL= FF, ZF= __

## Slide 243: Auxiliary Carry Flag. vIaiiVb
The Auxiliary Carry (AC) Flag indicates a carry or a borrow out of bit 3 to bit 4 in the destination operand.
Example:
MOV AL,0Fh MOV AL,22h
ADD AL, 1 ; ACF=1 SUB AL, 8h ;ACF=1
The develope
0 0 0 0 1 1 1 1 0 0 1 0 0 0 1 0
+ 0 0 0 0 0 0 0 1 - 0 0 0 0 1 0 0 0
0 0 0 1 0 0 0 0 0 0 0 1 1 0 1 0
Related operations: BCD (Binary-Coded Decimal) arithmetic operations in four bits. The digits 0..9 are represented en four bits.

## Slide 244: SIGN Flag (SF)
MOV CX,0
SUB CX,1 ; CX= -1, SF= 1, ZF= , CF=
ADD CX,2 ; CX= 1, SF= 0, ZF= , CF=
The SIGN flag is set when the destination signed operand is negative. The flag is clear when the destination is positive.
The SIGN flag is a copy of the destination's highest bit:
MOV AL,0
SUB AL,1 ; AL= 11111111b, SF= 1, ZF= , CF=
ADD AL,2 ; AL= 00000001b, SF= 0, ZF= , CF=

## Slide 245: Your turn . . .
MOV AX,00FFh
ADD AX,1 ; AX= SF= ZF= CF=
SUB AX,1 ; AX= SF= ZF= CF=
ADD AL,1 ; AL= SF= ZF= CF=
MOV BH,6Ch
ADD BH,95h ; BH= SF= ZF= CF=
MOV AL,2
SUB AL,3 ; AL= SF= ZF= CF=
For each of the following marked entries, show the values of the destination operand and the Sign, Zero, and Carry flags:

## Slide 246: OVERFLOW Flag (OF)
The OVERFLOW flag is set when the signed result of an operation is invalid or out of range.
; Example 1
MOV AL,+127
ADD AL,1 ; OF=__, AL=__, CF=__, SF=__, ZF=__
; Example 2
MOV AL,7Fh ; OF=__, AL= __
ADD AL,1

## Slide 247: A Rule of Thumb / signed
When ADDing two integers, remember that the Overflow flag is only set when . . .
  two positive operands are added and their sum is negative
  two negative operands are added and their sum is positive
What will be the values of the Overflow flag?
mov al,80h
add al,92h ; OF= , CF= , SF= , ZF=
mov al,-2
add al,+127 ; OF= , CF= , SF= , ZF=
mov al,+2
add al,+127 ; OF= , CF= , SF= , ZF=

## Slide 248: NEG Instruction.
.DATA
valB BYTE 1,0
valC SBYTE -128
.CODE
NEG valB ; CF= _, OF= _, SF= _, ZF= _
NEG [valB + 1] ; CF= _, OF= _, SF= _, ZF= _
NEG valC ; CF= _, OF= _, SF= _, ZF= _
The processor implements NEG using the following internal operation:
operand = 0 – operand ; or
operand = 0 + (-operand) ; adding viewpoint

## Slide 249: Your turn . . .
MOV AL,-128
NEG AL ; CF= , OF= , ZF= , SF=
MOV AX,8000h
ADD AX,2 ; CF= , OF= , ZF= , SF=
MOV AX,0
SUB AX,2 ; CF= , OF= , ZF= , SF=
MOV AL,-5
SUB AL,+125 ; CF= , OF= , ZF= , SF=
What will be the values of the given flags after each operation?

## Slide 250: Parity Flag. vIaiiVb
The Parity Flag (PF) is set when the least significant byte of the destination operand has an even number of 1 bits.
Example:
MOV AL, 10001100b
ADD AL, 00000010b ; AL = 10001110, PF = 1
SUB AL, 10000000b ; AL = 00001110, PF = 0

## Slide 251: Keeping track of Flags
Related instructions
LAHF – Load status flags into AH
    AH  Low byte of EFLAGS (S, Z, 0, A, 0, P, 1, C)
SAHF – Store AH into status flags
    Low byte of EFLAGS (S, Z, 0, A, 0, P, 1, C)  AH
.DATA
one BYTE ?
.CODE
LAHF
MOV one, AH
; following CODE
MOV BL, one
- - -
MOV AH, one
SAHF

## Slide 252: Instructions around the Carry flag
Set carry flag
    STC ;CF=1
Clear carry flag
    CLC ;CF=0
Complement carry flag
    CMC ;CF= 1s complement of CF
Add carry flag
    ADC opd1,opd2 ; opd1  opd1 + opd2 + CF

## Slide 253: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos
Agosto diciembre, 2022

## Slide 255: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 256: MS-MASM
MASM is the Microsoft Macro ASseMbler for x86 Intel processors.
  MASM is an x86 assembler that uses the Intel syntax for MS-DOS and MS-WINDOWS.
  There are two versions of the MASM:
    One (ML) for 16-bit and 32-bit assembly sources, and
    another (ML64) for 64-bit assembly sources only.

## Slide 257: Ejecución de Programas en Leng. Ensamblador
Flujo para ejecutar programas en Ensamblador:
  Ensamble con el Ensamblador MASM (Macro ASseMbler)
  Ligado o vinculado (linking) con el Linker
  Ejecución de programas en Lenguaje Ensamblador (Assembly)
file.asm
MASM
file.obj
file.exe
Linker
Programa fuente
Programa objeto
Programa ejecutable

## Slide 258: Arrancando Visual Studio 2019
En Windows:
Seleccionar:
Continue without code >

## Slide 259: Ventana de Visual Studio 2019
En Windows:

## Slide 260: Apertura del proyecto MASM 1
Proyecto PrjTtVS19rmt, previamente preparado para ensamblador, seleccionar:
  File > Open > Project / Solution
Seleccione la trayectoria de PrjTtVS19rmt de su computadora

## Slide 261: Apertura del proyecto MASM 2
Apareciendo
Seleccione Project.sln

## Slide 262: Apertura del proyecto MASM 3
Note: el nombre del fólder es PrjTtVS19rmt, el nombre del Solution Project es Project.sln , pero el ejecutable que se generara se llamara opc22pri31.exe

## Slide 263: Característica del proyecto
El fólder PrjTtVS19rmt, no lleva archivo fuente “.asm”:
Hay que agregarlo al Proyecto de manera “virtual”, siendo que el archive “.asm” se encuentra en otro folder, p.e. asmFilesa

## Slide 264: Agregado de un archivo “.asm”
Seleccione AddSub1.asm:
  Arrastrelo, y deposítelo sobre opc22pri31 en VS, o
  Haga copy, y paste sobre opc22pri31 en VS
Apareciendo dicho archive como sigue:

## Slide 265: Ensamblado (Assembling)
Ensamblado es la actividad, llevada a cabo por el Ensamblador (ml.exe), de traducir el archivo de entrada (.asm, programa fuente en Lenguaje Ensamblador) en un programa en Lenguaje Máquina, puesto en el archivo de salida (.obj, programa objeto).
El archivo de listado (.lst) es opcional.
Source program
file.asm
MASM
file.obj
Object program
file.lst
Listing file

## Slide 266: Ensamble del programa
Seleccione la línea de opc22pri31
Seleccione
Build > Build opc22pri31, o
Build > Rebuild opc22pri31
En la ventana de Output apareceran publicados lo errores en caso de existir.

## Slide 267: Archivo opc22pri31.lst
Ubicado en el folder clsB0\PrjTtVS19rmt
Se puede abrir con Bloq de Notas o Notepad++
¿Que contiene? _____

## Slide 268: Archivo .lst
Muestra la información que como el programa .asm fue ensamblado.
Contiene
  código fuente
  direcciones, offsets
  código objeto (languaje máquina)
  nombres de los segmentos
  símbolos (variables, procedimientos, y constantes)

## Slide 269: Ligado (Linking), lanzado por el ensamble
Ligado o vinculado , es la actividad, desarrollada por el Ligador (link.exe), de tomar el archivo objeto (.obj), revisando si el programa objeto contiene cualquier llamada a procedimientos o funciones de librería (del Sistema).
El ligador, agrega cualesquier procedimeinto o función de la librería, al programa ejecutable (.exe). El archivo ejecutable contiene el program a ser ejecutado por el Sistema Operativo.
file.obj
file.exe
Linker
Programa objeto
Programa ejecutable
library
Lista de procedures

## Slide 270: Running
Running, or the act where the CPU executes the executable program, first, the operating system loader utility reads the executable ﬁle into memory and branches the CPU to the program’s starting address, and the program begins to execute.
Command to run the executable program:
file.exe

## Slide 271: Ejecución del programa 1
Ubicarse en el folder clsB0\PrjTtVS19rmt\Debug
Doble click sobre Console.bat abriéndose la ventana, desde la cual prodra ejecutar el programa opc22pri31.exe

## Slide 272: Ejecución del programa 2

## Slide 273: Visualización y edición del “.asm”
Desde el Bloq de notas o Notepad++, o
Desde el mismo IDE del VS,
Tenga mucho cuidado, al modificarlo, de verificar que se guarde adecuadamente.

## Slide 274: Para finalizar
Cerrar la ventana de Console.bat
Remover el archive AddSub1.asm del Proyecto con
seleccionar AddSub1.asm, con botó derecho del ratón, y seleccionar Exclude from proyect
Volver a ensamblar Build > Rebuild opc22pri31 para que el Proyecto vuelva al estado inicial.

## Slide 275: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos
Agosto diciembre, 2022

## Slide 276: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 277: Operators in operands
Data-Related Operators in operands

## Slide 278: Data-Related Operators in Operands
Data-Related Operators are a kind of Directives, that are not executable instructions, instead they are only assembled by the assemblers (.CODE segment).
OFFSET Operator
TYPE Operator
LENGTHOF Operator
SIZEOF Operator
and more …

## Slide 279: OFFSET Operator
OFFSET returns the distance in bytes, of a label from the beginning of its enclosing DATA segment
  Protected mode: 32, 64 bits
  Real mode: 16 bits

## Slide 280: OFFSET Examples
.DATA
BYTE 404000h DUP(?)
bVal BYTE ?
wVal WORD ?
dVal DWORD ?
dVal2 DWORD ?
.CODE
MOV ESI,OFFSET bVal ; ESI = 00404000
MOV ESI,OFFSET wVal ; ESI = 00404001
MOV ESI,OFFSET dVal ; ESI = 0040____
MOV ESI,OFFSET dVal2 ; ESI = 0040____
Let's assume that the DATA segment begins at 00000000h:

## Slide 281: Relating to C/C++
// C++ version:
char array[1000];
char * p = array;
The value returned by OFFSET is a pointer. Compare the following code written for both C++ and assembly language:
; Assembly language:
.DATA
array BYTE 1000 DUP(?)
p DWORD ?
.CODE
MOV ESI,OFFSET array
MOV p, ESI

## Slide 282: Assembly Program Practice
ejerBB02a.asm
The running

## Slide 283: TYPE Operator
The TYPE operator returns the size, in bytes, of a single element of a data declaration.
.DATA
var1 BYTE ?
var2 WORD ?
var3 DWORD ?
var4 QWORD ?
.CODE
MOV EAX, TYPE var1 ; 1
MOV EAX, TYPE var2 ; 2
MOV EAX, TYPE var3 ; 4
MOV EAX, TYPE var4 ; _

## Slide 284: LENGTHOF Operator
.DATA LENGTHOF label
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 32
array2 WORD 5 DUP(3 DUP(?)) ; 15
array3 DWORD 1,2,3,4 ; 4
digitStr BYTE "12345678",0 ; 9
.CODE
MOV ECX, LENGTHOF array1 ; 32
MOV EBX, LENGTHOF digitStr ; 9
ADD EBX, TYPE digitStr ; __
MOV EAX, TYPE array3 ; __
The LENGTHOF operator counts the number of elements (magnitude) in a single data declaration.

## Slide 285: SIZEOF Operator
.DATA SIZEOF label
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 64
array2 WORD 5 DUP(3 DUP(?)) ; 30
array3 DWORD 1,2,3,4 ; 16
digitStr BYTE "12345678",0 ; 9
.CODE
MOV EAX,TYPE array1 ; __
MOV EBX,LENGTHOF array1 ; __
MOV ECX,SIZEOF array1 ; __
The SIZEOF operator returns a value (Bytes) that is equivalent to multiplying LENGTHOF by TYPE.

## Slide 286: Spanning Multiple Lines (1 of 2)
.DATA
array1 WORD 10,20
WORD 30,40
WORD 50,60
.CODE
mov eax, LENGTHOF array1 ; 2
mov ebx, SIZEOF array1 ; 4
In the following example, array1 identifies only the first WORD directive. Compare the values returned by LENGTHOF and SIZEOF here to those in the next slide:

## Slide 287: Spanning Multiple Lines (2 of 2)
.DATA
array1 WORD 10,20,
30,40,
50,60
.CODE
MOV EAX,LENGTHOF array1 ; 6
MOV EBX,SIZEOF array1 ; __
A data Directive spans multiple lines if each line (except the last) ends with a comma. The LENGTHOF and SIZEOF operators include all lines belonging to the same Directive:

## Slide 288: Symbols, Symbolic Constant
A symbol is an identifier.
    ValorFinal, Fecha23
Symbolic constant (is not a label)
  Is an identifier associated with a 32/64-bit integer expression (or constant)
  Syntax identifier = expression (“=“ equal-sign directive)
    ValorFinal = 452
    MOV EAX, ValorFinal (really MOV EAX, 452)

## Slide 289: Symbols, Symbolic Constant - 2
Symbols do not reserve storage.
Symbols are not labels.
Symbols only exist during the time while the Assembler is Assembling a program in Assembly Language.

## Slide 290: Symbolic Constants
May be redifined
    ValorFinal = 483
    MOV EAX, ValorFinal ; really MOV EAX, 483
    ValorFinal = 627
    MOV EAX, ValorFinal ; really MOV EAX, 627
Why use Symbols? Clarifies the program
    Better when you see ValorFinal instead of 483
    EscKey = 27
    MOV AL, EscKey ; really MOV EAX, 27

## Slide 291: Assembly Program Practice
ejerBB03a.asm
The running

## Slide 292: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos
Agosto - diciembre 2022

## Slide 293: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 294: Program structure
TITLE primer
;Descripcion del programa, fecha, versión
INCLUDE Irvine32.inc ;libreria de funciones; falta agregar más
.DATA
; directivas de almacenamiento y tipos de datos
.CODE
main PROC ; Inicia el procedimiento main
; instrucciones, mnemónicos
main ENDP ; Termina el procedimiento principal
END main ; Termina el area de Ensamble

## Slide 295: Irvine32 Library Procedures
INCLUDE Irvine32.inc ; chapter 5
These procedures are for I/Os
DumpRegs
DumpMem
ReadInt
ReadHex
WriteInt
WriteHex
WriteString
Crlf
ReadString
Notes: Irvine Procedures (Procedimientos propios del autor)
Call es para llamar a los procedimientos en general.
Invoke es para llamar procedimientos propios de Windows.
Se pueden usar indistintamente.

## Slide 296: DumpRegs
DumpRegs
  It desplays all the general registers and the flags.
Sample call
.CODE
MOV ECX, 0
CALL DumpRegs
MOV EAX, 8Fh
CALL DumpRegs
Notes: Imprime todos los registros después de alguna operación.

## Slide 297: DumpRegs example

## Slide 298: DumpMem
DumpMem
  It writes a range/block of memory to the console window in hexadecimal.
  Pass, in ESI the starting address of the block, in ECX the number of units or elements, and in EBX the unit size (1 : byte, 2 : word, 4 : doubleword).
Sample call
.DATA
array DWORD 11, 12, 13
.CODE
MOV ESI, OFFSET array
MOV ECX, 3 ; ? ________
MOV EBX, 4 ; ? ________
CALL DumpMem
Notes: DWORD 4 bytes
11:
0B
00
00
00
12:
0C
00
00
00
13:
0D
00
00
00

## Slide 299: WriteInt
WriteInt
  Writes a 32-bit signed integer to the console window in decimal format with a leading sign and no leading zeros.
  Pass the integer into EAX.
Sample
.DATA
valInt SDWORD -317432
.CODE
MOV EAX, valInt
CALL WriteInt
CALL Crlf
MOV EAX, 235896
CALL WriteInt
Notes: CRLF--> Carriag Return and Line Feed
(Nueva línea)

## Slide 300: WriteHex
WriteHex
  Writes a 32-bit unsigned integer to the console window in 8-digit hexadecimal format.
  Leading zeroes are inserted if necessary.
  Pass the integer into EAX.
Sample
.DATA
valHex DWORD 6ABCh
.CODE
MOV EAX, valHex
CALL WriteHex
CALL Crlf
MOV EAX, 8EF9h
CALL WriteHex

## Slide 301: WriteString
WriteString
  It writes a null-terminated string to the console window.
  Pass, in EDX register, the string’s offset.
Sample call
.DATA
line1 BYTE “Enter the data: “, 0
.CODE
MOV EDX, OFFSET line
CALL WriteString

## Slide 302: Crlf
Crlf
  It advances the cursor, inwindow console, to the beginning of the next line.
  It writes down a string containing the ASCII characters 0Dh and 0Ah.
  0Dh is the code of CR (Carriage Return, Enter) and 0Ah is the code of LF (Line Feed).
  Check out the appendices 8-bit ASCII Code tables.
Sample call
.DATA
line1 BYTE “Enter the data: “, 0
.CODE
MOV EDX, OFFSET line
CALL WriteString
CALL Crlf

## Slide 303: ReadInt
ReadInt
  Reads a 32-bit signed integer from the keyboard and returns the value in EAX register.
  Can be typed an optional leading plus or minus sign.
  It sets the Overflow flag and display an error message if the value cannot be represented as a 32-bit signed integer (-2,147,483,648 to + 2,147,483,647)
Sample
.DATA
valInt SDWORD ?
.CODE
CALL ReadInt
MOV valInt, EAX

## Slide 304: ReadHex
ReadHex
  Reads a 32-bit hexadecimal integer from the keyboard and returns the value in EAX register.
  No error checking is performed for invalid characteres.
  Can use both uppercase letters and lowercase letters for the digits A through F.
Sample
.DATA
valHex DWORD ?
.CODE
CALL ReadHex
MOV valHex, EAX

## Slide 305: ReadString
ReadString
  It reads a string from the keyboard, stopping when the user types the ENTER key.
  Pass the buffer’s offset in EDX register.
  Set ECX to the maximum number of characters that the user can type, plus 1 to save space for the terminting null byte.
  It returns, in EAX, the count of the number of characters typed by the user.
Sample
.DATA
bufferR BYTE 81 DUP(0) ; 80 characters plus 0 (terminator)
charCountR DWORD ?
.CODE
MOV EDX, OFFSET bufferR
MOV ECX, 81
CALL ReadString
MOV charCountR, EAX

## Slide 306: 8-bit ASCII Codes: 0-127

## Slide 307: 8-bit ASCII Codes: 128-255

## Slide 308: Review these procedures
Chapter 5 (5.4.2, 5.4.3)
Clrscr
ReadChar, ReadDec, ReadKey
WriteBin, WriteBinB
WriteChar, WriteDec, WriteHexB

## Slide 309: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos
Agosto - diciembre 2022

## Slide 310: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 311: Memory storage of values
.DATA
Alfa DWORD 12345678h
; How is the DWORD stored in memory?
; Other ways to storage the same values
Beta WORD __...__
Delta BYTE __...__

## Slide 312: Mapping data values
Mapping smaller data Registers inside longer data registers: e.g. AL, AH <>AX <> EAX, or, DL, DH <>DX <> EDX
What if now we start to do data mapping with memory storage locations?
Two ways for mapping:
Label Directive / Data Segment
“PTR” operator / Code Segment

## Slide 313: LABEL Directive
assigns a label, with type and data value(s), the one to be mapped (e.g. zeta)
  assigns an alternate label-name and type to an existing storage location, the mapping one
  does not allocate any storage of its own. Symbol table?
.DATA
gamma LABEL DWORD ; no storage
epsilon LABEL WORD ; no storage
zeta BYTE 00h,10h,00h,20h ; storage
.CODE
mov EAX, gamma ; 20001000h
mov CX, epsilon ; 1000h
mov DL, zeta ; 00h

## Slide 314: “type” PTR – Operand Operator
“type” PTR operator:
  overrides the declared size (“type”) of an operand.
  allows the selection of some part of a defined variable (label, variable).
It works in the section .CODE
Operand operator (“type” PTR) that works at assembly time (like directives TYPE, LENGTHOF, etc.).
Similar concept: HLL casting

## Slide 315: “type” PTR - Operator Examples 1
.DATA
myDouble DWORD 12345678h
.CODE
MOV EAX, myDouble ; EAX =
MOV AX, myDouble ; error – why?
MOV AX, WORD PTR myDouble ; loads 5678h
MOV WORD PTR myDouble, 4A9Bh ; saves 4A9Bh
MOV AL, BYTE PTR myDouble ; AL =
MOV AL, BYTE PTR [myDouble+1] ; AL =
MOV AL, BYTE PTR [myDouble+2] ; AL =
MOV AL, BYTE PTR [myDouble+3] ; AL =
MOV AX, WORD PTR myDouble ; AX =
MOV AX, WORD PTR [myDouble+2] ; AX =

## Slide 316: “type” PTR - Operator Examples 2
.DATA
myBytes BYTE 12h,34h,56h,78h
.CODE
MOV AX, WORD PTR [myBytes] ; AX =
MOV AX, WORD PTR [myBytes+2] ; AX =
MOV EAX, DWORD PTR myBytes ; EAX =
PTR can also be used to combine elements of a smaller data type and move them into a larger operand. The CPU will automatically consider the bytes in little-endian format.

## Slide 317: “type” PTR - Operator Examples 3
.DATA
varB BYTE 65h,31h,02h,05h
varW WORD 6543h,1202h
varD DWORD 12345678h
.CODE
MOV AX, WORD PTR [varB+2] ; a.
MOV BL, BYTE PTR varD ; b.
MOV BL, BYTE PTR [varW+2] ; c.
MOV AX, WORD PTR [varD+2] ; d.
MOV EAX, DWORD PTR varW ; e.
AX=
BL=
BL=
AX=
EAX=

## Slide 318: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos, bxf
Agosto - diciembre 2022

## Slide 319: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 320: Multiplication and Division
Multiplication and Division Instructions
MUL – unsigned multiply
IMUL – signed multiply
DIV – unsigned division
IDIV – signed división

## Slide 321: MUL Instruction (Unsigned Multiply) iiVa
The MUL (unsigned multiply) instruction multiplies an 8-, 16-, 32- or 64- bit operand by either AL, AX, EAX, or RAX.
The one-operand instruction formats are:
    MUL reg/mem8 ;16-bit product
    MUL reg/mem16 ;32-bit product
    MUL reg/mem32 ;64-bit product
Implicit multiplicand: AL, AX or EAX.
Check CARRY flag after MUL for significant bits in the upper half of the product.
The product is twice the size of the multiplicand or the multiplier.
Multiplicand | Multiplier | Product
AL | reg/mem8 | AH:AL = AL * reg/mem8
AX | reg/mem16 | DX:AX = AX * reg/mem16
EAX | reg/mem32 | EDX:EAX = EAX * reg/mem32

## Slide 322: MUL Examples 1
2000h * 100h, using 16-bit operands:
.DATA
val1 WORD 2000h
val2 WORD 100h
.CODE
MOV AX,val1
MUL val2 ; DX:AX = 00200000h, CF=1
The CARRY flag indicates whether or not the upper half of the product contains significant digits.
MOV EAX,12345h
MOV EBX,1000h
MUL EBX ; EDX:EAX = 0000000012345000h, CF=0
12345h * 1000h, using 32-bit operands:

## Slide 323: MUL Examples 2
5h * 10h, using 8-bit operands:
.CODE
MOV AL,05h
MOV BL,10h
MUL BL ; AH:AL = 0050h, CF=0

## Slide 324: Your turn . . . 1
MOV AX,1234h
MOV BX,100h
MUL BX
What will be the hexadecimal values of DX, AX, and the Carry flag after the following instructions execute?
Diego:
  AX = 1234h
  BX = 100h
  DX:AX = AX * BX = 1234h * 100h
   DX:AX = 0012:3400h  CF = 1

## Slide 325: Your turn . . . 2
MOV EAX,00128765h
MOV ECX,10000h
MUL ECX
What will be the hexadecimal values of EDX, EAX, and the Carry flag after the following instructions execute?
Diego:
  EAX = 00128765h
  ECX = 10000h
  EDX:EAX = EAX * ECX = 00128765h * 10000h
   DX:AX = 00000012 : 87650000h  CF = 1

## Slide 326: IMUL Instruction (Signed Multiply)
IMUL (signed integer multiply ) multiplies an 8-, 16-, 32- or 64- bit operand by either AL, AX, EAX, or RAX.
Preserves the sign of the product by sign-extending it into the upper half of the destination register
The one-operand instruction formats are:
    IMUL reg/mem8 IMUL reg/mem32
    IMUL reg/mem16 IMUL reg/mem64
CF and OF are set if the upper half of the product is not a sign extension of the lower half.
Multiplicand | Multiplier | Product
AL | reg/mem8 | AH:AL = AL * reg/mem8
AX | reg/mem16 | DX:AX = AX * reg/mem16
EAX | reg/mem32 | EDX:EAX = EAX * reg/mem32

## Slide 327: IMUL Examples
Example: multiply 48 * 4, using 8-bit operands:
MOV AL,48 ; AL = 48 = 30h
MOV BL,4
IMUL BL ; AX(AH:AL) = 00C0h, OF=1
OF=1 because AH is not a sign extension of AL.
Example: multiply 48 * 4, using 16-bit operands:
MOV AX,48
MOV BX,4
IMUL BX ; DX:AX = 000000C0h, OF=0
OF=0 because DX is a sign extension of AX.

## Slide 328: IMUL Instruction (Signed Multiply)
Two-operand 16-bit formats, 16-bit product:
    IMUL reg16,reg/mem16
    IMUL reg16,imm8
    IMUL reg16,imm16
Two-operand 32-bit formats, 32-bit product:
    IMUL reg32,reg/mem32
    IMUL reg32,imm8
    IMUL reg32,imm32
Two-operand 64-bit formats.
Multiplicand | Multiplier | Product
reg16 | reg/mem16 | reg16 = reg16 * reg/mem16
reg16 | imm8/imm16 | reg16 = reg16 * imm8/imm16
reg32 | reg/mem32 | reg32 = reg32 * reg/mem32
reg32 | imm8/imm32 | reg32 = reg32 * imm8/imm32
Two-operand IMUL formats truncate the product. When significant digits are lost OF and CF are set.

## Slide 329: IMUL Instruction (Signed Multiply)
Three-operand 16-bit formats:
    IMUL reg16,reg/mem16,imm8
    IMUL reg16,reg/mem16,imm16
Three-operand 32-bit formats:
    IMUL reg32,reg/mem32,imm8
    IMUL reg32,reg/mem32,imm32
Three-operand 64-bit formats.
Multiplicand | Multiplier | Product
reg16 | reg/mem16 | reg16 = reg/mem16 * imm8
reg16 | imm8/imm16 | reg16 = reg/mem16 * imm16
reg32 | reg/mem32 | reg32 = reg/mem32 * imm8
reg32 | imm8/imm32 | reg32 = reg/mem32 * imm32
Three-operand IMUL formats truncate the product. When significant digits are lost OF and CF are set.

## Slide 330: IMUL Examples
Example: multiply 4,823,424 * -423:
MOV EAX,4823424
MOV EBX,-423
IMUL EBX ; EDX:EAX = FFFFFFFF86635D80h, OF=0
OF=0, CF=0 because EDX is a sign extension of EAX.

## Slide 331: Your turn . . . 3
MOV AX,8760h
MOV BX,100h
IMUL BX
What will be the hexadecimal values of DX, AX, and the OVERFLOW flag after the following instructions execute?

## Slide 332: DIV Instruction (Unsigned Divide)
The DIV (unsigned divide) instruction performs 8-bit, 16-bit, 32-bit and 64-bit division on unsigned integers
A single operand is supplied (register or memory operand), which is assumed to be the divisor
Instruction formats:
    DIV reg/mem8 ;16-bit dividend
    DIV reg/mem16 ;32-bit dividend
    DIV reg/mem32 ;64-bit dividend
    DIV reg/mem64
Dividend | Divisor | Quotient | Reminder
AH:AL | reg/mem8 | AL | AH
DX:AX | reg/mem16 | AX | DX
EDX:EAX | reg/mem32 | EAX | EDX

## Slide 333: DIV Examples
Divide 8003h by 100h, using 16-bit operands, 32-bit dividend
MOV DX,0 ; clear dividend, high
MOV AX,8003h ; dividend, low
MOV CX,100h ; divisor
DIV CX ; AX = 0080h, DX = 3
Same division, using 32-bit operands, 64-bit dividend:
MOV EDX,0 ; clear dividend, high
MOV EAX,8003h ; dividend, low
MOV ECX,100h ; divisor
DIV ECX ; EAX = 00000080h, EDX = 3

## Slide 334: DIV conditions
All arithmetic status flag values are undefined (?) after executing DIV instructions.
What happens if the Quotient doesn’t fit the destination operand (register)?
  A divide overflow condition results, causing a CPU interrupt and the current program halts.
What happens if the divisor is zero?
  A division by zero condition results, causing a CPU interrupt and the current program halts.
  To prevent division by zero, test de divisor before dividing.

## Slide 335: Your turn . . . 4
MOV DX,0087h
MOV AX,6000h
MOV BX,100h
DIV BX
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:

## Slide 336: Your turn . . . 5
MOV DX,0087h
MOV AX,6002h
MOV BX,10h
DIV BX
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:

## Slide 337: Signed Integer Division (IDIV)
Signed integers must be sign-extended before division takes place
  fill high byte/word/doubleword with a copy of the low byte/word/doubleword's sign bit
For example, the high byte contains a copy of the sign bit from the low byte:

## Slide 338: CBW, CWD, CDQ Instructions
The CBW, CWD, and CDQ instructions provide important sign-extension operations:
  CBW (convert byte to word) extends AL into AH
  CWD (convert word to dword) extends AX into DX
  CDQ (convert dword to qword) extends EAX into EDX
  CQO (convert qword to oword) extends RAX into RDX
Example:
    .DATA
    dwordVal SDWORD -101 ; FFFFFF9Bh
    .CODE
    MOV EAX,dwordVal
    CDQ ; EDX:EAX = FFFFFFFFFFFFFF9Bh

## Slide 339: IDIV Instruction
IDIV (signed divide) performs signed integer division
Same syntax and operands as DIV instruction
Example: 8-bit division of –48 by 5
MOV AL,-48 ; AL = D0h (-30h)
CBW ; extend AL into AH=FFh
MOV BL,5
IDIV BL ; AL = -9, AH = -3

## Slide 340: IDIV Examples
Example: 32-bit division of –48 by 5
MOV EAX,-48 ; EAX = FFFFFFD0h
CDQ ; extend EAX into EDX
MOV EBX,5
IDIV EBX ; EAX = -9, EDX = -3
Example: 16-bit division of –48 by 5
MOV AX,-48 ; AX = FFD0h
CWD ; extend AX into DX
MOV BX,5
IDIV BX ; AX = -9, DX = -3

## Slide 341: Your turn . . . 6
MOV AX,0FDFFh ;AX= -513 = -0201h
CWD
MOV BX,100h ;BX= 256
IDIV BX
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:

## Slide 342: IDIV conditions
All arithmetic status flag values are undefined (?) after executing IDIV instructions.
What happens if the Quotient doesn’t fit the destination operand (register)?
  A divide overflow condition results, causing a CPU interrupt and the current program halts.
What happens if the divisor is zero?
  A division by zero condition results, causing a CPU interrupt and the current program halts.
  To prevent division by zero, test de divisor before dividing.

## Slide 343: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos, bxh
Agosto – diciembre 2022

## Slide 344: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 345: Transfer of Control Instructions
Transfer of Control Unit (jumps) Instructions
Unconditional or Imperative
    jump instruction: JMP
    goto, in the beginning of the HLL
Conditional
    conditional jump instructions: Jcond family

## Slide 346: CPU Conceptual Map
status flags
ALU
conditional jumps
branching logic
arithmetic & bitwise operations
part of
used by
provide
attached to
affect
CU
executes next
executes

## Slide 347: Jump instruction
JMP instruction
Causes an unconditional transfer of control (jump) to a destination (label:), inside .CODE.
This destination (label:) is translated like an offset.
Syntax: JMP label
Logic: EIP  OFFSET label
Examples:
.CODE
lbl2:
instrucA
instrucB
JMP lbl2
.CODE
JMP lbl3
instrucR
instrucT
lbl3:

## Slide 348: Conditional Jump instructions
Jcond instructions
The conditional transfer (Jcond) to a destination (label:), inside .CODE, jumps, only if the condition of a flag, or several flags are met.
Remember, only ALU instructrions (arithmetic, or logic) can modify several or all flags.

## Slide 349: HLL Structured instructions. via
Algorithm ---- program
Structured thinking
Algorithm structures or Structured instructions
    Selectives: If-then, if-then-else, switch-case
    Repetitives: while, for, do-while, repeat
There are not such instructions in machine language.
The programmer must implement those algorithm structures.

## Slide 350: HLL structures need jumps? via
IF-THEN
IF-THEN-ELSE
WHILE / FOR
DO-WHILE

## Slide 351: Conditional Jump instructions
A conditional jump instruction (Jcond) branches to a label:, when a specific flag or several flag conditions are met.
The Jcond analyze the CPU status flags affected by the last executed ALU instruction.
Some conditional jumps:
  JC - jump to a label if the Carry flag is set
  JZ - jump to a label if the Zero flag is set
  JS - jump to a label if the Sign flag is set

## Slide 352: Jconds usage
Example 1
(IF-ELSE)
Example2
(DO-WHILE)
instrucChgFlags
Jcond la1
. . .
. . .
la1:. . .
la2:
. . .
. . .
instrucChgFlags
Jcond la2
. . .

## Slide 353: Jconds Based on one Flag (after instruction)

## Slide 354: Jconds examples
Example 1
Example2
MOV EAX,1
SUB EAX,1
JZ la1
. . .
la1:. . .
la2:
. . .
MOV EAX,1
ADD EAX,1
JNC la2
. . .

## Slide 355: Flags to Test for a Jcond?
How many flags have to be tested for a Jcond, when implementing a Boolean Expression of a HLL’s Algorithm Structure (if, while, …)?
For unsigned expressions?
  Chiefly, CF and ZF
For signed expressions?
  Mainly, SF and OF

## Slide 356: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto – diciembre 2022

## Slide 357: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 358: Jconds
Hard to use them, because the predecessor instructions usually affect several flags at the same time, not necessaraly one flag.

## Slide 359: CMP in Structured Instructions
CMP instruction is used to create conditional logic structures
When follow CMP with a conditional jump instruction, the result is the assembly language equivalent of an IF or a WHILE statement, or any other structured High Level Language instruction.

## Slide 360: CMP Instruction
Syntax: CMP leftOp, rightOp
Compares the leftOp operand to the rightOp operand
  Nondestructive implied subtraction of rightOp from leftOp (neither operand is changed)
Logic: leftOp - rightOp
The comparation affect all the flags.
The following operand combinations are permitted
  CMP reg, reg
  CMP reg, mem
  CMP reg, imm
  CMP mem, reg
  CMP mem, imm

## Slide 361: CMP + Jconds usage
Example 1 looks like an IF
Example2 looks like repetitive
cmp EAX,uno
Jcond la1
. . .
. . .
la1:. . .
la2:
. . .
. . .
cmp dos,EBX
Jcond la2
. . .

## Slide 362: CMP of two Unsigned operands
Example 1: it works when leftOp == rightOp
MOV AL,5
CMP AL,5 ; ZF=1, CF=0
Example 2: it works when leftOp < rightOp
MOV AL,4
CMP AL,5 ; ZF=0, CF=1
Example 3: it works when leftOp > rightOp
MOV AL,6
CMP AL,5 ; ZF = 0, CF = 0

## Slide 363: Jconds Based on Equality
For UNSIGNED or SIGNED use.

## Slide 364: Jconds Based on Unsigned operands
Better use JA, JAE, JB and JBE Above, Below

## Slide 365: Examples, Unsigned- 1
CMP EAX,EBX
JA Larger ; above
Task: Jump to a label Larger if unsigned EAX is greater than EBX
Solution: Use CMP, followed by JA
CMP EAX,Val1
JBE L1 ; below or equal
Jump to label L1 if unsigned EAX is less than or equal to Val1

## Slide 366: CMP of two Signed operands
Example 4: it works when leftOp > rightOp
mov al,5
cmp al,-2 ; Sign flag == Overflow flag
Example 5: it works when leftOp < rightOp
mov al,-1
cmp al,5 ; Sign flag != Overflow flag
Example 6: it works when leftOp == rightOp
mov al,-1
cmp al,-1 ; ZF=1, CF=don´t care

## Slide 367: Jconds Based on Signed operands
Better use JG, JGE, JL and JLE Greater, Lower

## Slide 368: Examples, Signed- 2
CMP EAX,EBX
JG Greater
Task: Jump to a label Greater if signed EAX is greater than EBX
Solution: Use CMP, followed by JG
CMP EAX,Val1
JLE L1
Jump to label L1 if signed EAX is less than or equal to Val1

## Slide 369: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto – diciembre 2022

## Slide 370: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 371: IF-then, IF-then-else, While, DO-while, user implementation, in Assembly

## Slide 372: IF-then implementation
  High Level L Assembly
  IF(LfOp cmpOpr RhOp) CMP LfOp, RhOp
  { JnoCMP outIF
  block. .; block. .
} outIF: ;next instruc
The IF Assembly implementation involves a conditional jump for the negative of the comparison (JnoCMP)

## Slide 373: IF-then examples
  High Level L Assembly
  Large = BX; MOV Large,BX
  IF(AX > BX) CMP AX,BX
  { JBE outIF ;Jump if AX<=BX
  Large = AX; MOV Large,AX ; AX>BX
} outIF:
Compare unsigned AX to BX, and copy the larger of the two into a variable named Large
  High Level L Assembly
  Small = AX; MOV Small,AX
  IF(BX < AX) CMP BX,AX
  { JGE outIF ;Jump if BX>=AX
  Small = BX; MOV Small,BX ;BX<AX
} outIF:
Compare signed AX to BX, and copy the smaller of the two into a variable named Small

## Slide 374: IF-then-else implementation
  High Level L Assembly
  IF(LfOp cmpOp RhOp) CMP LfOp,RhOp
  { JnoCMP inELSE
  block1. .; block1. .
} JMP outIF
else inELSE:
{
black2. .; block2. .
} outIF: ;next instruc
The IF Assembly implementation involves a conditional jump for the negative of the comparison (JnoCMP). A JMP is needed at the end of block1 to avoid enter into the ELSE area.

## Slide 375: WHILE implementation
  High Level L Assembly
  WHILE(LfOp cmpOp RhOp) inWHILE: CMP LfOp,RhOp
  { JnoCMP outWHILE
  block. .; block. .
} JMP inWhile
outWHILE: ;nextinstruc
The WHILE Assembly implementation involves a conditional jump for the negative of the comparison (JnoCMP). After the block it requieres to jump back (JMP) to do compare.

## Slide 376: WHILE example
  High Level L Assembly
  EAX=45; MOV EAX,45
  EBX=1; MOV EBX,1
  WHILE(EBX < 6) inWHILE: CMP EBX,6
  { JGE outWHILE
  EAX=EAX-2; SUB EAX,2
  EBX=EBX+1; INC EBX
} JMP inWhile
outWHILE: ;nextinstruc
The WHILE Assembly implementation involves a conditional jump for the negative of the comparison (JnoCMP). After the block it requires to jump back to do compare. Example signed.

## Slide 377: DO-WHILE implementation
  High Level L Assembly
  DO inDO:
  block. .; block. .
  WHILE(LfOp cmpOp RhOp) CMP LfOp,RhOp
  JsaCMP inDO
;nextinstruc
The DO-WHILE Assembly implementation involves a conditional jump for the same comparison (JsaCMP). After the block it requires to jump back to do compare.

## Slide 378: DO-WHILE example
  High Level L Assembly
  EAX=50; MOV EAX,50
  EBX=0; MOV EBX,0
  DO inDO:
  EAX=EAX+1; INC EAX
  EBX=EBX+1; INC EBX
  WHILE(EBX < 4) CMP EBX,4
  JL inDO
;nextinstruc
The DO-WHILE Assembly implementation involves a conditional jump for the positive of the comparison (JsaCMP). After the block it requires to jump back to do compare. Example signed.

## Slide 379: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto – diciembre 2022

## Slide 380: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 381: HLL Boolean Operators
Logical Operators, for Boolean operations:
  Boolean values: true (1d= 0…01b) / false (0d= 0…0b)
  NOT: !a (!true>false, !false>true)
  AND: a && b
  OR: a || b
Bitwise Operators, for bit-to-bit operations:
  Integer-bit values: n bits (8, 16, 32, 64, … bits)
  NOT: ~c (complement 1s)
  AND: d & e
  OR: d | e
  XOR: d ^ e

## Slide 382: Bitwise Boolean Instructions
Issue: there are not logical Boolean ASSEMBLY Instructions,
Only Bitwise (bit to bit computations): AND, OR, XOR, NOT, TEST

## Slide 383: AND Instruction
AND, bitwise, bit to bit
Syntax: AND destination, source
The following operand combinations are permitted
  AND reg, reg
  AND reg, mem
  AND reg, imm
  AND mem, reg
  AND mem, imm
Operands can be 8, 16, 32, or 64 bits, must be same size
Bit masking with the source operand.
Set INTERSECTION of bits

## Slide 384: AND Instruction
Performs a Boolean AND operation between each pair of matching bits in two operands
Flags
  Clears Overflow, Carry
  Modifies Sign, Zero, and Parity
Syntax:
    AND destination, source
  (same operand types as MOV)
AND
Bit masking, source: 0 in source clears a bit, 1 leaves it unchanged.

## Slide 385: OR Instruction
OR, bitwise, bit to bit
Syntax: OR destination, source
The following operand combinations are permitted
  OR reg, reg
  OR reg, mem
  OR reg, imm
  OR mem, reg
  OR mem, imm
Operands can be 8, 16, 32, or 64 bits, must be same size
Useful when you want to set one or more bits without affecting the other bits
Set UNION of bits

## Slide 386: OR Instruction
Performs a Boolean OR operation between each pair of matching bits in two operands
Flags
  Clears Overflow, Carry
  Modifies Sign, Zero, and Parity
Syntax:
    OR destination, source
OR
1 in source set a bit, 0 leaves it unchanged.

## Slide 387: XOR Instruction
Performs a Boolean eXclusive-OR bitwise operation between each pair of matching bits in two operands
XOR with 0 retains its value, with 1 reverses value
Flags
  Clears Overflow, Carry
  Modifies Sign, Zero, and Parity
Syntax:
    XOR destination, source
XOR
XOR is a useful way to toggle (invert) the bits in an operand.

## Slide 388: NOT Instruction
Performs a Boolean NOT bitwise operation on a single destination operand
The following operand combinations are permitted
  NOT reg
  NOT mem
Flags
  No flags are affected
Syntax:
    NOT destination
NOT
Results called one’s complement
Set COMPLEMENT of bits

## Slide 389: Bit-Mapped Set Operations
Set Complement
    MOV AL, SetB ; AL= SetB= 0000 0111b
    NOT AL ; AL= 1111 1000b
Set Intersection
    MOV AL, SetB ; AL= SetB= 0000 0111b
    AND AL, SetS ; SetS= 0110 0011b AL= 0000 0011b
Set Union
    MOV AL, SetB ; AL= SetB= 0000 0111b
    OR EAX, SetS ; SetS= 0110 0011b AL= 0110 0111b

## Slide 390: ASCII Code

## Slide 391: Applications (1 of 4)
mov al, 'a' ; AL = 01100001b, ‘a’
and al, 11011111b ; AL = 01000001b, ‘A’
Task: Convert the character in AL to UPPER CASE.
Solution: Use the AND instruction to clear bit 5.

## Slide 392: Applications (2 of 4)
MOV AL,6 ; AL = 00000110b, 6
OR AL,00110000b ; AL = 00110110b, ‘6’
Task: Convert a binary decimal byte into its equivalent ASCII Decimal Digit.
Solution: Use the OR instruction to set bits 4 and 5.
The ASCII digit '6' = 00110110b

## Slide 393: Applications (3 of 4)
MOV AX, wordVal
AND AX, 1 ; low bit set?
JZ EvenValue ; jump if Zero flag set
Task: Jump to a label if an integer is even.
Solution: AND the lowest bit with a 1. If the result is Zero, the number was even.
Your turn: Write code that jumps to a label if an integer is negative.

## Slide 394: Applications (4 of 4)
OR AL,AL
JNZ IsNotZero ; jump if not zero
Task: Jump to a label if the value in AL is not zero.
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction.
ORing any number with itself does not change its value.

## Slide 395: TEST Instruction
Performs a nondestructive AND bitwise operation between each pair of matching bits in two operands
No operands are modified.
Always clears the Overflow and Carry flags.
Modifies the Sign, Zero, and Parity flags.
Example: jump to a label if either bit 0 or bit 1 in AL is set.
TEST AL,00000011b
JNZ ValueFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set.
TEST AL,00000011b
JZ ValueNotFound
TEST AL,03h
JNZ ValueFound

## Slide 396: Example
The value 0000 0011 in this example is called a bit mask.
TEST AL,00000011b
0 0 1 0 0 1 0 1 <- AL input value
0 0 0 0 0 0 1 1 <- test value
0 0 0 0 0 0 0 1 <- result: ZF = 0
TEST AL,00001001b
0 0 1 0 0 1 0 0 <- AL input value
0 0 0 0 1 0 0 1 <- test value
0 0 0 0 0 0 0 0 <- result: ZF = 1
The value 0000 1001 in this example is called a bit mask.

## Slide 397: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto – diciembre 2022

## Slide 398: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 399: HLL’s COMPOUND EXPRESSIONS in CONDITIONAL STRUCTURES

## Slide 400: Bitwise Boolean Instructions
To build up compound conditional expressions for IF-THEN, IF-THEN-ELSE, WHILE, DO-WHILE, REPEAT-UNTIL and FOR, logical Boolean instructions are required.
  E.g.
    (A > B) && (C <= 5)
    && is the Logical Boolean operator and, in a HLL

## Slide 401: Compound Expression with AND - 1
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the First expression is false, the Second expression is skipped:
if (al > bl) AND (bl > cl)
X = 1;

## Slide 402: Compound Expression with AND - 2
cmp al,bl ; First expression...
JA L1 true
JMP next ;false :: a1<=b1
L1:
cmp bl,cl ; Second expression...
JA L2 ; true
JMP next false
L2: ; both are true
mov X,1 ; set X to 1
next:
if (al > bl) AND (bl > cl)
X = 1;
This is one possible implementation . . . no sign

## Slide 403: Compound Expression with AND - 3
cmp al,bl ; First expression...
JBE next ; quit if false
cmp bl,cl ; Second expression...
JBE next ; quit if false
mov X,1 ; both are true
next:
if (al > bl) AND (bl > cl)
X = 1;
But the following implementation uses 29% less code by reversing the first relational operator. We allow the program to "fall through" to the second expression:

## Slide 404: Compound Expression with AND - 4
Implement the following pseudocode in assembly language. All values are unsigned:
  cmp ebx,ecx
  JA next
  cmp ecx,edx
  JBE next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx
&& ecx > edx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 405: Compound Expression with OR - 1
When implementing the logical OR operator, consider that HLLs use short-circuit evaluation
In the following example, if the First expression is true, the Second expression is skipped:
if (al > bl) OR (bl > cl)
X = 1;

## Slide 406: Compound Expression with OR - 2
cmp al,bl ; is AL > BL?
JA L1 ; yes
cmp bl,cl ; no: is BL > CL?
JBE next ; no: skip next statement
L1:
mov X,1 ; set X to 1
next:
We can use "fall-through" logic to keep the code as short as possible:
if (al > bl) OR (bl > cl)
X = 1;

## Slide 407: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto – diciembre 2022

## Slide 408: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 409: MACRO Procedure
MACRO (DIRECTIVE)
A MACRO procedure is a named block of Assembly Language instructions.
Every time that this named block is invoked , Assembler during preprocessing step, expands a copy of the block, of instructions, into the programe code.
The expanded code is passed to the assembly step, where it is checked for correctness.
Macro-Directives, in Section 10.2, Irvine.

## Slide 410: Defining a Macro
A macro must be defined before it can be used.
Parameters are optional.
Each parameter follows the rules for identifiers. It is a string that is assigned a value when the macro is invoked.
Syntax:
macroname MACRO [parameter-1, parameter-2,...]
statement-list
ENDM

## Slide 411: mNewLine Macro - an example
; Macro definition
mNewLine MACRO
CALL CrLf
ENDM
.DATA
.CODE
mNewLine
; Assembler program, after initial
; preprocessing Assembly step
; mNewLine is expanded out
.DATA
.CODE
CALL CrLf

## Slide 412: mPutchar Macro - an example
; Macro definition with an argument
mPutchar MACRO char
push EAX
mov AL, char
call WriteChar
pop EAX
ENDM
.DATA
.CODE
mPutchar ‘A’
; Assembler program, after initial
; preprocessing Assembly step
; mPutchar ‘A’ is expanded out
.DATA
.CODE
push EAX
mov AL, ‘A’
call WriteChar
pop EAX

## Slide 413: Invoking Macros
When you invoke a macro, each argument you pass matches a declared parameter.
Each parameter is replaced by its corresponding argument when the macro is expanded.
When a macro expands, it generates assembly language source code.
Arguments are treated as simple text by the preprocessor.

## Slide 414: mWriteStr Macro - an example
; Macro definition with an argument
mWriteStr MACRO buffer
PUSH EDX
MOV EDX, OFFSET buffer
CALL WriteString
POP EDX
ENDM
.DATA
str1 BYTE "Welcome!", 0
.CODE
mWriteStr str1
; Assembler program, after initial
; preprocessing Assembly step
; mWriteStr str1 is expanded out
.DATA
str1 BYTE "Welcome!", 0
.CODE
PUSH EDX
MOV EDX, OFFSET str1
CALL WriteString
POP EDX

## Slide 415: mDumpMem Macro - an example
mDumpMem MACRO address, itemsCount, itemSize
push ebx
push ecx
push esi
mov esi,address
mov ecx,itemsCount
mov ebx,itemSize
call DumpMem
pop esi
pop ecx
pop ebx
ENDM
The mDumpMem macro streamlines calls to the link library's DumpMem procedure.

## Slide 416: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto - diciembre 2022

## Slide 417: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 418: CONDITIONAL CONTROL FLOW MACRO DIRECTIVES
SELECTIVES
.IF condition, .ELSE, .ELSEIF condition, .ENDIF
REPETITIVES
.WHILE condition, .ENDW
.REPEAT, .UNTIL condition
.BREAK, .CONTINUE, used with .WHILE and .REPEAT
Macro-Directives, in Section 6.7, Irvine.

## Slide 419: Conditional Control Flow Directives
Directive | Description
.BREAK | Generates code to terminate a .WHILE or .REPEAT block
.CONTINUE | Generates code to jump to the top of a .WHILE or .REPEAT block
.ELSE | Begins block of statements to execute when the .IF condition is false
.ELSEIF condition | Generates code that tests condition and executes statements that follow, until an .ENDIF directive or another .ELSEIF directive is found
.ENDIF | Terminates a block of statements following an .IF, .ELSE, or .ELSEIF directive
.ENDW | Terminates a block of statements following a .WHILE directive
.IF condition | Generates code that executes the block of statements if condition is true.
.REPEAT | Generates code that repeats execution of the block of statements until condition becomes true
.UNTIL condition | Generates code that repeats the block of statements between .REPEAT and .UNTIL until condition becomes true
.WHILE condition | Generates code that executes the block of statements between .WHILE and .ENDW as long as condition is true

## Slide 420: .IF family macro-directives
.IF eax > ebx
mov edx,1
.ELSE
mov edx,2
.ENDIF
.IF, .ELSE, .ELSEIF, and .ENDIF can be used to evaluate runtime expressions and create block-structured IF statements.
Assembly examples:
MASM generates (macro-expands) "hidden" code for you, consisting of code labels, CMP and conditional jump instructions, and replacing arguments.
.IF eax > ebx && eax > ecx
mov edx,1
.ELSE
mov edx,2
.ENDIF

## Slide 421: Relational and Logical Operators

## Slide 422: AND and OR: Compound Expressions
When using any directive, the || is the logical OR
  .IF expression1 || expression2
  Statements . . .
  .ENDIF
When using any directive, the && symbol is the logical AND
  .IF expression1 && expression2
  Statements . . .
  .ENDIF

## Slide 423: Expression examples
eax > 10000h
val1 <= 100
val2 == eax
val3 != ebx
(eax > 0) && (eax > 10000h)
(val1 <= 100) || (val2 <= 100)
(val2 != ebx) && !CARRY?
(dl < 0) || (dl > 79)

## Slide 424: Signed and Unsigned Comparisons - 1
mov EAX,6
cmp EAX,val1
JBE @C0001
mov result,1
@C0001:
.DATA
val1 DWORD 5
result DWORD ?
.CODE
mov EAX,6
.IF EAX > val1
mov result,1
.ENDIF
Expanded code:
MASM automatically generates an unsigned jump (JBE) because val1 is unsigned.

## Slide 425: Signed and Unsigned Comparisons - 2
mov EAX,6
cmp EAX,val1
JLE @C0001
mov result,1
@C0001:
.DATA
val1 SDWORD 5
result SDWORD ?
.CODE
mov EAX,6
.IF EAX > val1
mov result,1
.ENDIF
Expanded code:
MASM automatically generates a signed jump (JLE) because val1 is signed.

## Slide 426: Signed and Unsigned Comparisons - 3
mov EBX,5
mov EAX,6
cmp EAX,EBX
JBE @C0001
mov result,1
@C0001:
.DATA
result DWORD ?
.CODE
mov EBX,5
mov EAX,6
.IF EAX > EBX
mov result,1
.ENDIF
Expanded code:
MASM automatically generates an unsigned jump (JBE) when both operands are registers . . .

## Slide 427: Signed and Unsigned Comparisons - 4
mov EBX,5
mov EAX,6
cmp EAX,EBX
JLE @C0001
mov result,1
@C0001:
.DATA
result SDWORD ?
.CODE
mov EBX,5
mov EAX,6
.IF SDWORD PTR EAX > EBX
mov result,1
.ENDIF
Expanded code:
. . . unless you prefix one of the register operands with the type PTR operator. Then a signed jump is generated.

## Slide 428: Example 1
SetCursorPosition PROC
; Sets the cursor position.
; Receives: DL = X-coordinate, DH = Y-coordinate.
; Checks the ranges of DL and DH.
; Returns: nothing
; ------------------------------------------------
. DATA
BadXCoordMsg BYTE " X-Coordinate out of range! " , 0Dh, 0Ah, 0
BadYCoordMsg BYTE " Y-Coordinate out of range! " , 0Dh, 0Ah, 0
. CODE
.IF ( dl < 0 ) | | ( dl > 79 )
mov edx, OFFSET BadXCoordMsg
call WriteString
jmp quit
.ENDIF
.IF ( dh < 0 ) | | ( dh > 24)
mov edx, OFFSET BadYCoordMsg
call WriteString
jmp quit
.ENDIF
call Gotoxy
quit:
ret
SetCursorPosition ENDP
. CODE
; .IF ( dl < 0 ) | | ( dl > 79 )
cmp dl, 000h
jb @C0002
cmp dl, 04Fh
jbe @C0001
@C0002 :
mov edx, OFFSET BadXCoordMsg
call WriteString
jmp quit
; . ENDIF
@C0001:
; .IF ( dh < 0 ) | | ( dh > 24)
cmp dh, 000h
jb @C0005
cmp dh, 018h
jbe @C0004
@C0005:
mov edx, OFFSET BadYCoordMsg
call WriteString
jmp quit
; .ENDIF
@C0004:
call Gotoxy
quit:
ret

## Slide 429: Example 2
; Determine registration based on two criteria:
; Average Grade
; Credits the person wants to take
.DATA
TRUE = 1
FALSE = 0
gradeAverage WORD 275 ; test value
credits WORD 12 ; test value
OkToRegister BYTE ?
.CODE
mov OkToRegister, FALSE
.IF gradeAverage > 350
movOkToRegister, TRUE
.ELSEIF (gradeAverage > 250 ) && ( credits <= 16)
mov OkToRegister, TRUE
.ELSEIF ( credits <= 12 )
mov OkToRegister, TRUE
.ENDIF
mov byte ptr OkToRegister, FALSE
;.IF gradeAverage > 350
cmp word ptr gradeAverage, 350
jbe @C0006
mov byte ptr OkToRegister, TRUE
jmp @C0008
@C0006:
;.ELSEIF (gradeAverage > 250 ) && ( credits <= 16)
cmp word ptr gradeAverage, 250
jbe @C0009
cmp word ptr credits, 16
ja @C0009
mov byte ptr OkToRegister, TRUE
jmp @C0008
@C0009 :
;.ELSEIF ( credits <= 12 )
cmp word ptr credits, 12
ja @C0008
mov byte ptr OkToRegister, TRUE
@C0008:
;.ENDIF

## Slide 430: .WHILE family directives
Tests the loop condition before executing the loop body The .ENDW directive marks the end of the loop.
.WHILE condition
statements
.ENDW
Example:
; Display integers 1 – 10:
mov EAX,0
.WHILE EAX < 10
inc EAX
call WriteDec
call Crlf
.ENDW

## Slide 431: .REPEAT family directives
Executes the loop body before testing the loop condition associated with the .UNTIL directive.
.REPEAT
statements
.UNTIL condition
Example:
; Display integers 1 – 10:
mov EAX,0
.REPEAT
inc EAX
call WriteDec
call Crlf
.UNTIL EAX == 10

## Slide 432: Example 3: .WHILE nesting an .IF
;HLL
while( op1 < op2 )
{
op1++;
if( op1 == op3 )
X = 2 ;
else
X = 3 ;
}
;ASM
. DATA
X DWORD 0
op1 DWORD 2 ; test data
op2 DWORD 4 ; test data
op3 DWORD 5 ; test data
. CODE
mov eax, op1
.WHILE eax < op2
inc eax
mov op1, eax
.IF eax == op3
mov X, 2
.ELSE
mov X, 3
.ENDIF
.ENDW

## Slide 433: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto - diciembre 2022

## Slide 434: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 435: STACK
STACK data structure
A STACK of values (data)
  values are only added to the top (PUSH operation)
  values are only removed from the top (POP operation)
  LIFO (Last-in, First-out) data structure

## Slide 436: Process memory space and resources
0x00000000
0xFFFFFFFF
Memory address space
Code section
(text segment)
static data section
(data segment)
heap
(dynamic allocated mem)
Runtime STACK
(storage call returns, etc.)
OS resources
(open files, network connect.,
Sound channels, …)
CPU
General Registers
PC
SP
EIP
ESP
CS >
DS >
SS >

## Slide 437: Runtime STACK
STACK inside every Process
Managed by the CPU, using a stack pointer register
  ESP (Extended Stack Pointer)
    ESP always points to the last value added

## Slide 438: PUSH Instruction
PUSH syntax, one operand
  PUSH reg/mem16 ; for 2-Byte, 16-bit operand
  PUSH reg/mem32 ; for 4-Byte, 32-bit operand
  PUSH reg/mem64 ; for 8-Byte, 64-bit operand
  PUSH imm32 ; for 4-Byte, 32-bit operand
  PUSH imm64 ; for 8-Byte, 64-bit operand

## Slide 439: PUSH operation 1
A PUSH operation decrements the stack pointer by nByOp (2 [16 bits], 4 [32 bits] or 8 Bytes [64 bits]), and copies a value into the location pointed to by the stack pointer ESP.
    ESP  ESP – nByOp ; nByOp=4 Bytes, a 32-bit operand
    STACK [ESP]  reg/var/value

## Slide 440: PUSH operation 2
Same stack after pushing two more integers:
The stack grows downward. The area below ESP is always available (unless the stack has overflowed).

## Slide 441: POP Instruction
POP syntax, one operand
  POP reg/mem16 ; for 2-Byte, 16-bit operand
  POP reg/mem32 ; for 4-Byte, 32-bit operand
  POP reg/mem64 ; for 8-Byte, 64-bit operand

## Slide 442: POP Operation
Copies value at STACK[ESP] into a register or variable.
  Reg/Var  STACK[ESP]
Adds n to ESP, where n is either 2, 4 or 8.
  value of n depends on the attribute of the operand receiving the data
  ESP  ESP + n

## Slide 443: Using PUSH and POP
Save and restore registers when they contain important values. PUSH and POP instructions occur in the opposite order.
.DATA
dwordVal DWORD 675
.CODE
PUSH ESI ; push registers
PUSH ECX
PUSH EBX
MOV ESI,OFFSET dwordVal ; display some memory
MOV ECX,LENGTHOF dwordVal
MOV EBX,TYPE dwordVal
CALL DumpMem
POP EBX ; restore registers
POP ECX ; aware of LIFO
POP ESI

## Slide 444: Related Instructions
PUSHFD and POPFD
  push and pop the EFLAGS register (32-bit)
PUSHAD pushes the 32-bit general-purpose registers on the stack
  order: EAX, ECX, EDX, EBX, ESP, EBP, ESI, EDI
POPAD pops the same registers off the stack in reverse order
PUSHA and POPA, do the same for 16-bit registers
  order: AX, CX, DX, BX, SP, BP, SI, DI

## Slide 445: PUSHAD
The value pushed for the ESP register is its value before prior to pushing the first register.
Temporary = ESP;
Push(EAX);
Push(ECX);
Push(EDX);
Push(EBX);
Push(Temporary);
Push(EBP);
Push(ESI);
Push(EDI);

## Slide 446: POPAD
The ESP register is incremented after each register is loaded.
EDI = Pop(); ESP=ESP+4
ESI = Pop(); ESP=ESP+4
EBP = Pop(); ESP=ESP+4
ESP = ESP + 4; //skip next 4 bytes of stack
EBX = Pop(); ESP=ESP+4
EDX = Pop(); ESP=ESP+4
ECX = Pop(); ESP=ESP+4
EAX = Pop(); ESP=ESP+4

## Slide 447: Stack applications
Temporary save area for registers, once the registers end a set of operations, their original values can be restored.
The stack provides temporary storage for local variables.
The Call for a procedure, saves an address that uses up the Return of the procedure called.
HLL: The formal parameters and the automatic variables

## Slide 448: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto – diciembre 2022

## Slide 449: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2022

## Slide 450: Addressing Modes
Addressing Mode.
  refers to the way, in which, the CPU accesses the effective values from the operand(s) of an instruction
Two general Addressing Modes:
  Direct Addressing (seen up to now)
  Indirect Addressing

## Slide 451: Direct Addressing Mode
With DIRECT addressing mode, in Operands
  The operand has the location to place an effective value, or has the content to get an effective value,
  Examples
    mov EAX, alfa
    mov beta, EBX
    mov alfa, 354
    Direct Addressing Operands
      Register Direct O.: EAX, EBX (location or content)
      Memory Direct O.: alfa, beta (location or content)
      Immediate Direct O: 354 (content)

## Slide 452: Indirect Addressing Mode -1
With INDIRECT addressing mode, in operands
  The operand has the memory address (offset) of the location to place a value, or has the memory address (offset) of the content to get a value
  It means, the operand has a pointer (or a reference)
  Example using pseudo-code - 1
    mov ESI, OFFSET beta
    mov EAX, ind{ESI}

## Slide 453: Indirect Addressing Mode -2
  Example using pseudo-code - 2
    add ESI, 4
    mov EAX, ind{ESI}

## Slide 454: Indirect Addressing Modes -3
Two approaches
Indirect Operands
  [reg]
    reg contains an address (offset, pointer, or reference)
Indexed Operands
  Coming soon!

## Slide 455: Indirect Operands - 1
reg: could be any general-purpose register
  Rmn, . . ., EAX, EBX, ECX, EDX ( 64, 32, 16, and 8 bits )
  Rxy, . . ., ESI, EDI, EBP, ESP (64, 32 and 16 bits)
ESI and EDI prefered registers
  RSI, ESI: Source Index
  RDI, EDI: Destination Index
For each approach?
  How come, you get the effective address? ____
  How long (bits) must be the effective address? ____
  What TYPE must be the location or the content? ____

## Slide 456: Indirect Operands - 2
An indirect operand holds the address of a variable (pointer, offset, or reference), usually an ARRAY or STRING.
It can be dereferenced (just like a pointer).
In Protected Mode, any indirect operand can be any of the 32-bit or 64-bit general-purpose registers, surrounded by brackets.
Also, a memory place (DWORD / QWORD) can hold an address value.
General Protection Fault: in Protected Mode, if the effective address, points to an area outside your program’s data segment, the CPU executes a General Protection Fault (GP).

## Slide 457: Indirect Operands - 3a
.DATA
val1 BYTE 10h,20h,30h
.CODE
MOV ESI,OFFSET val1
MOV AL,[ESI] ; ESI=0000 0000h; AL = 10h
; Size of the location?___
; Size of the content?___
INC ESI
MOV AL,[ESI] ; ESI=0000 ____h; AL = 20h
INC ESI
MOV AL,[ESI] ; ESI=0000 ____h; AL = 30h
An indirect operand holds the address of a variable, usually an array or string. It can be dereferenced (just like a pointer).

## Slide 458: Indirect Operands - 3b
.DATA
myCount WORD 0
.CODE
MOV ESI,OFFSET myCount
INC [ESI] ; error: ambiguous
INC WORD PTR [ESI] ; ok
Use PTR to clarify the size attribute of a memory operand.
Should PTR be used here?
ADD [ESI],20
yes, because [ESI] could point to a byte, word, or doubleword

## Slide 459: Pointers - 3c
.DATA
BYTE 16 DUP(?)
arrayW WORD 1000h,2000h,3000h
ptrW DWORD arrayW
.CODE
MOV ESI, ptrW
MOV AX,[ESI] ; AX = 1000h
You can declare a pointer variable that contains the offset of another variable (it must be 32-bit or 64-bit long).
Alternate format:
ptrW DWORD OFFSET arrayW

## Slide 460: Array Sum Example - 3d
.DATA
arrayW WORD 1000h,2000h,3000h
.CODE
  MOV ESI,OFFSET arrayW
  MOV AX,[ESI]
  ADD ESI,2 ;or better: ADD ESI,TYPE arrayW
  ADD AX,[ESI]
  ADD ESI,2
  ADD AX,[ESI] ; AX = sum of the array
Indirect operands are ideal for traversing an array. Note that the register in brackets must be incremented by a value that matches the array type.

## Slide 461: Direct and Indirect operands
Direct operands in two-operand instructions (f.i. CMP)
  CMP reg, reg
  CMP reg, mem
  CMP reg, imm
  CMP mem, reg
  CMP mem, imm
Indirect operands in two-operand instructions (f.i. CMP)
  CMP reg, [reg] like direct operand CMP reg, ___
  CMP [reg], reg like direct operand CMP ___, reg
  CMP [reg], imm like direct operand CMP ___, imm

## Slide 462: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
Agosto - diciembre 2022